|  | PRESS RELEASE |
| --- | --- |

CTIA warns: Scooter can break during driving

(Prague, September 11, 2012) The Czech Trade Inspection Authority warns against another dangerous scooter which was found in the offer in the inner market. It is the third of the products taken for laboratory assessment of safety in the frame of the control action focused on scooters which shows serious deficiencies. When the strength of the handles was tested, the folding mechanism broke where the handling system is connected to the board and the belt fixing the rear wheel broke as well which is why the scooter poses a risk of serious injury to the smallest users who could fall over the handles in case the defect would occur while driving. The scooter named simply Scooter also shows other deficiencies from the stipulated technical characteristics and thus is dangerous.

We speak about this product:

Scooter

Manufacturer/country of origin: Made in China

Importer: Not stated

Dangers

When the strength of the handlebar was tested, the folding mechanism broke where the riding system is connected to the board and sharp edges and tips appeared (see picture 1).

Within the test of strength, the metal belt fixing the rear wheel broke as well (picture 2).

In the hinged part, there are holes in which a stick of 5 mm in average can fit, but it is not possible to put in a stick of the average of 12 mm (see picture 3); the average of the endings of the handles is 32.9 mm (the requirement is minimally 40 mm).

The average of the front wheel is 97.7 mm (the requirement is minimally 120 mm).

With regard to the numerous detected deficiencies it is more that probable that a child could get seriously injured when using the product in a common and predictable way.

The CTIA banned selling of the Scooter and the distributor subsequently withdrew the product from the market.

Further information can be found on the website of the CTIA www.coi.cz or at the communication department of the CTIA.