|  | PRESS RELEASE |
| --- | --- |

CTIA: LPG with excessive sulphur content again on sale

(Results of fuel quality monitoring in August 2014)

(Prague, September 17, 2014) LPG samples were without deviations from required quality in July, however in August the Czech Trade Inspection Authority detected that three samples of the fuel type collected in North Moravia failed the required quality. Two samples again contained excessive amount of sulphur and one could contain undesirable admixtures as indicated by lower octane number. This was 1.5% of the total number of 213 inspected samples of motor fuels collected at filling stations on the whole territory of the Czech Republic. Despite the good results of other fuel types, inspections carried out by the Czech Trade Inspection Authority continue through further collection of samples and inspections of motor fuels based on consumers’ submissions.

The Czech Trade Inspection Authority collected samples of automotive petrol, diesel fuel, diesel fuel blend, bio fuel, LPG, CNG, and Ethanol E85 within monitoring of fuel quality pursuit to the Act No. 311/2006 Coll. and the Decree No. 133/2010 Coll. at filling stations on the whole territory of the Czech Republic.

Inspection results

3 of the total number of 203 samples of motor fuels collected and inspected in August failed stipulated quality requirements, i.e. 1.5%. In August 2014, defects in collected and inspected LPG samples were detected.

LPG for engine

3 of 24 collected and inspected samples of LPG for engine failed the quality requirements of the applicable technical standard. Laboratory tests showed higher values of sulphur, namely 75.0 mg/kg and 105.0 mg/kg (maximal value of the quality indicator is 60.0 mg/kg when measurement uncertainty is taken into account). Deviation could be caused by different composition as a result of production defect or intentional manipulation. Value of motor octane number (MON) was 88.3% in one sample of LPG for engine was measured. The lowest value of this quality indicator shall be 88.8 when measurement uncertainty is taken into account.

Bio fuels

Laboratory analysis didn’t show any violation of the upper acceptable limit of content of bio ingredients in the inspected fuels. Content of fatty acid methyl ester was inspected in 90 samples of diesel fuel. Content of ethanol was inspected in 74 samples of automotive petrol.

Prohibition of sale of poor quality fuels

In August 2014, selling of motor fuels was prohibited in three cases because they failed to comply with requirements of applicable quality standards. The measure was imposed on 7,420.5 l of LPG for engine in the total amount of 130,833.60.

Conclusion

In comparison with results of the previous month, the rate of poor quality motor fuel samples was higher by 0.6% in August as a result of deviations from stipulated quality detected within LPG for engine. Samples of other collected motor fuels didn’t show any deviations from parameters of applicable technical standards.

Results according to inspectorates

Legend: COLL = collected, N = noncompliant

Attachments:  	Monitoring of fuel quality in August 2014

Monitoring of fuel quality from January to August 2014