CTIA: Three diesel samples failed concerning flash point

(Monitoring of fuel quality in January 2015)

(Prague, February 19, 2015) From the start of January 2015, monitoring of fuel quality has continued at filling stations on the whole territory of the Czech Republic, including subsequent inspection sampling. Only three diesel fuel samples out of all 235 collected fuel samples failed, namely concerning flash point. This quality parameter was 10°C lower than stipulated in the applicable technical standard (which is 53°C). We speak about so called negligence deviation that suggests that fuel was contaminated by petrol. Lower flashpoint poses a risk of reduction of viscosity of diesel fuel and worsening its lubricity. Prohibition was imposed on sale of about 39.000 litres of poor quality diesel fuel in two cases and administrative proceedings will be launched with operators of filling stations where noncompliant fuel was detected.

Sampling of automotive petrol, diesel fuel, diesel fuel blend, bio fuels, LPG, and CNG as well as inspecting of their quality continued in compliance with the Act No. 311/2006 Coll. on Fuels). 3 out of 235 samples collected in January 2015 failed quality requirements, i.e. 1.3%. Defects were detected only concerning collected and inspected diesel samples.

| Collected fuels according to types - January 2015 |
| --- |
| Fuel type | Collected samples | In % | Noncompliant samples | % of fuel type |
| Automotive petrol | 92 | 39.1 | 0 | 0.0 |
| Diesel fuel | 102 | 43.4 | 3 | 2.9 |
| Diesel fuel blend | 2 | 0.9 | 0 | 0.0 |
| FAME | 2 | 0.9 | 0 | 0.0 |
| LPG | 32 | 13.6 | 0 | 0.0 |
| CNG | 5 | 2.1 | 0 | 0.0 |
| Ethanol E85 | 0 | 0.0 | 0 | 0.0 |
| Total | 235 | 100.0 | 3 | 1.3 |

Diesel fuel

In January, CTIA inspectors collected and inspected 102 samples of diesel fuel in total, including 3 samples that failed quality requirements of the applicable technical standard concerning the quality indicator flash point. Values of two samples were 43°C and measuring of the third sample showed 46.5°C when minimal required value is 53°C when measurement uncertainty is taken into account. Other samples of this fuel complied concerning all indicators as stipulated in the technical standard ČSN EN 590 – Motor fuels – Diesel fuel – Technical Requirements and Test Methods..

Organic components in fuels

Content of fatty acid methyl ester was inspected in 102 diesel fuel samples. Ethanol content was inspected in 92 automotive petrol samples. The upper acceptable limit of content of organic components was not detected within laboratory analysis.

Measure taken

In 2 cases, the Czech Trade Inspection Authority imposed measures consisting of prohibition of sale of motor fuels that didn’t comply with requirements of special legal regulations (pursuant to section 7 par. 1 letter b) of the Act No. 64/1986 Coll. on CTIA) . Prohibition of further sale was imposed on 38,831.4 litres of diesel fuel amounting to 1,436,699 CZK until remedy would be made.

Conclusion

Analysis of samples of diesel fuels collected in January 2015 proved deviations from quality standards in cases of three diesel fuel samples. The ratio of poor quality fuels decreased from 1.5% to 1.3% when compared with December 2014.

Results according to inspectorates

Attachments: 	Monitoring of fuel quality in January 2015