|  | PRESS RELEASE |
| --- | --- |

Frog with magnet is a dangerous toy!

(Prague, March 11, 2015) Children are exposed to risk of health damage during play with a frog with magnet. The Czech Trade Inspection Authority detected that vendors in the Czech Republic offer a product which poses serious health risk especially to children. Legs of the little frog were released from the body after minimal power was used. When playing with the toy, children could inhale or swallow the released small parts and thus could block their airways or injure internal organs. After necessary documentation is elaborated, the toys will be notified into the system RAPEX.

Frog with magnet

No. 74815

Manufacturer: unknown

Importer: unknown

Risk type: Health risk

Risks:

All 4 legs and the small frog separated when the power of 9 to15 N was used within a pull test – which is less than the standard’s requirement (90±2 N). Released parts all fit in the tube for small parts.

A child can be injured when playing with the product in a usual and predictable way (swallowing or inhalation of separated small parts and airways obstruction or injury to internal organs).

Imposed measures

The Czech Trade Inspection Authority prohibited sale of the frog with magnet and distributor took action and withdrew the product from the market. All documents necessary for notification of this dangerous toy into the RAPEX system will be transferred for further elaboration to the contact point at the Ministry of Industry and Trade.