|  | PRESS RELEASE |
| --- | --- |

SANTA gives hits from electric current instead of gifts

(Prague, November 9, 2015) The Czech Trade Inspection Authority detected an electric light chain with a Santa Claus cover which is offered in the Czech market and poses serious risk of injury to consumers. The danger consists of possible release of its connecting wires from the control unit’s desktop and subsequent uncovering of living parts. Such contact would cause injury by electric current. Proportions of the two-pole power cord plug don’t comply with determined model. The light chain isn’t equipped with obligatory information which can lead to injuries in the consequence of incorrect way of use of this product. The Czech Trade Inspection Authority prohibited distribution of this dangerous chain and ordered its withdrawal from the market.

Light chain SANTA

Manufacturer/importer: unknown

It is a light chain with a picture of Santa Claus, unchangeable light sources, equipped with electronics for light effects – interrupted lighting with various intervals in various parts of the chain. The product is equipped with power cord with a two-pole plug connected to the electric unit. Functions of the light effects are set automatically, so the consumer isn’t allowed to influence them as the electric unit isn’t equipped with any control elements. The lighting part of the chain is placed in a plastic decorative cover with a picture of Santa. Manufacturer is unknown, the product is not equipped with any accompanying documentation or data on the packaging. The two-pole cord is marked with the following information: 2,5 A 250 V. The following marking is on the electric unit: LX-01, 12 V-240 V, 50/60 Hz and CE marking which fails graphics of the model determined for marking of selected products.

Danger

The danger of injury by electric current is posed in case when connecting wires release from the desktop of the control unit and uncover living parts. Subsequent user’s touch would cause injury by electric current. Proportions of the two-pole power cord plug don’t comply with the determined model. The product isn’t accompanied with all obligatory information which poses a risk to user’s health in case of incorrect use of the product.

Imposed measure

The Czech Trade Inspection Authority prohibited distribution of the product and imposed the inspected person to withdraw the dangerous light chain from distribution.