|  | PRESS RELEASE |
| --- | --- |

Whistling owl contained phthalates and small parts

(Prague, December 15, 2015) During monitoring of the market with toys, CTIA inspectors detected a toy intended for smallest users which failed requirements for safety. A whistling owl with no information about its manufacturer and origin contained small parts as well as excessive content of dangerous phthalates DEHP – the content was up to 140 times higher. The Czech Trade Inspection Authority ordered the distributor to withdraw the particular toy from the market and the owl was notified into the database of dangerous products RAPEX, file No. A12/1307/15.

Whistling owl feifei

Manufacturer:		unknown

Country of origin:	unknown

EAN:			6952426522335

Original product within sale

Product description

The pink toy made from softened plastic has a white whistling equipment in its below part. The toy is sold in a plastic net, equipped with a paper label displaying the CE marking and a text “feifei toys”.

Dangers

The product failed safety requirements for toys. Laboratory assessment proved presence of Bis (2ethylhexyl) phthalate – DEHP – in the toy’s material. This substance shall not be used in higher content that 0.1% of weight as a substance or admixture of substances in softened plastic materials that are used within production of toys and child care products. The tested sample contained 14.1±0.9% of weight according to the results of the laboratory assessment.

It cannot be excluded that within usual use the DEHP, as a substance with a negative influence on healthy development of small children, can release from the toy.

This toy also failed minimal requirements for toys safety as stipulated in the applicable technical standard (EN 71-1:2011 + A3:2014 of articles 5.1 – General Requirements, and 5.8 – Shape and Size of Certain Toys), because the whistling equipment can be separated from the toy when the power of 31.5 N is used. The separated whistle is a small part that can be easily inhaled or swallowed by a child.

Small part released from the toy within a laboratory test

Within usual and predictable way of use it cannot be excluded that a situation occurs when a small child releases the whistling mechanism within game. This small part could cause serious health problems if inhaled.

Taken measures

In order to prevent further distribution of the product which fails technical requirements for safety and health, the Czech Trade Inspection Authority imposed a protective measure on the inspected person. All information about the dangerous toy were published in the pan-European database RAPEX, file No. A12/1307/15.