|  | PRESS RELEASE |
| --- | --- |

Playpen Baby Maxi isn’t safe enough

(Prague, January 22, 2016) During inspections of child care products, the Czech Trade Inspection Authority found out that a playpen which poses a serious safety hazard to smallest users is sold in the market. A wooden pin on the upper door side, being a part of the locking mechanism, repeatedly collapsed during laboratory tests. In the consequence, a small part occurred which could fit into the test tube for small parts, so it could endanger child’s health if inhaled or suffocated. The hazard of finger clash or contusion is posed by cutting spaces in the lower part of closed doors as well as in the area of hinges when the doors are opened. Complex documentation concerning the dangerous playpen was transferred to the RAPEX contact point and published in the database under the notification number A12/1674/15.

Playpen – BABY MAXI, model 445

Manufacturer:		unknown

Importer:		SisCom S.C., Gdaňsk

Product name: 		BABY MAXI

Model:                              445

Original product as constructed in the test room

Product description

Classic wooden octagon-shaped playpen with a gate. Individual wooden parts are red, yellow, blue and green.

Danger

The playpen has two mechanisms for securing the doors – locking detent on the lower side of the doors and a wooden pin on the upper side. The two mechanisms must be used simultaneously. During tests, however, the wooden pin repeatedly released and could fit into the test tube for small parts. Another risk of injury was caused by two spaces in the lower part of the doors through which a probe of the diameter of 7 mm went through, but through which a probe of the diameter of 12 mm didn’t go through. When opening the doors, another cutting space appeared in the pin area where door parts got as close as less than 12 mm.

Within a usual and predictable way of use of the product, a situation cannot be excluded that a child swallows or inhales the released wooden pin. There is a hazard of child’s fingers injury if the child puts his fingers to the cutting space between the doors and his own body when opening or closing the doors.

Conclusion

Professional assessment showed that the classic wooden playpen with a gate Baby Maxi, model 445, fails the requirements of the Act No. 102/2001 Coll. on General Safety of Products. Numerous defects significantly influencing the product’s safety were detected during tests carried out in the laboratory pursuant to requirements of the applicable European standard ČSN EN 12227.

Taken action

The Czech Trade Inspection Authority imposed protective measure on the inspected final distributors, namely immediate withdrawal of the product from distribution. All available documents and information about the dangerous children’s playpen were transferred to the contact point at the Ministry of Industry and Trade and published in the pan-European database RAPEX under notification number A12/1674/15.