|  | PRESS RELEASE |
| --- | --- |

Folding SCOOTER is dangerous to children

(Prague, January 28, 2016) Within monitoring of the market with toys CTIA inspectors spotted a folding scooter originating in China which poses a risk of injury to smallest users. This product has various colour variants with a rabbit on the footboard and on the tube. Injury hazard is posed during game and ride at several places: adjustable and folding handlebar don’t have the required diameter, covers are removable without the necessity to use any power and wholes are accessible, so fingers can be injured. Spaces between the wheels and the toy’s body are not wide enough to prevent finger clashes. The steering tube with handlebar collapsed within the laboratory strength test. The Czech Trade Inspection Authority immediately ordered withdrawal of the product from distribution and handed over the documentation to the system RAPEX. Information about this dangerous toy were published under the number A12/0028/16:

Children’s folding scooter - SCOOTER

Manufacturer:			unknown

Importer:			T-N hračky domácí potřeby, s. r. o., ČR

Product name on packaging: 	Scooter

Product name on label: 	Skateboard - Koloběžka

Model: 				Item No. Jrl 204033

EAN on label:			6900012040336

Country of origin:		made in China

Original product in sale

Product description

Folding scooter with one front and two rear wheels was offered in various colours (red and green). Coloured children’s motives with a rabbit with a crown were displayed on the steering tube and the footboard. The toy was delivered in a cardboard box with red, white and blue printing while the picture of a scooter was different than the product folded inside. Only the following warning was displayed on the label on the box: „Pozor: Nevhodné pro děti do 3 let z rizika polknutí malých částí.“  (“Watch out: Unsuitable for children under 3 years – risk of swallowing of small parts.”)

Danger

The product failed requirements of the Government Order No. 86/2011 Coll. on Technical Requirements for Toys, Act No. 22/1997 Coll. on General Safety of Products because it failed the following requirements for safety as determined in the applicable standard ČSN EN 71-1:2011 + A3:2014:

- Black protective covers of handle tips were separable without the necessity to use any power (minimal requirements is 60 N pursuant to Article 4.9 - Protruding parts);

- Diameter of the handle ends was 33 mm despite the required minimal required proportion is 40 mm pursuant to Article 4.15.5.7 - Protruding parts);

- Fingers can be put into accessible adjustable and folding handlebars (Article 4.15.5.4);

- A stick of the diameter 5 mm can be inserted to the gaps between the wheels and the toy’s body while the stick of the diameter of 12 mm cannot be inserted at the same time (pursuant to Article 4.15.1.6 – Transmission and wheel arrangement;

- Insufficient strength of the handlebar (pursuant to Article 4.15.5.3 – Strength). Two defects occurred within strength test. During one of the tests the handlebar separated in two parts and the steering tube with handlebar collapsed when loaded.

It is probable that during usual and predictable way of use or during game with this particular scooter the above mentioned defects can result in dangerous situations posing risk of injury to children. There is a hazard of injury in the consequence of fingers getting stuck in the wholes during manipulation with the scooter or in the consequence of a fall caused by insufficient strength of the used material and mounting of the handlebar and its protective covers.

Taken measure

The Czech Trade Inspection Authority imposed a protective measure to the trader who was ordered to withdraw the product from distribution immediately in order to prevent further sale of the same products that fail the technical requirements for toys. All information about the dangerous scooter were published in the system RAPEX, notification number A12/0028/16.