|  | PRESS RELEASE |
| --- | --- |

Two fuel samples failed in January

(Monitoring of fuel quality in 2016)

(Prague, February 22, 2016) In January, the Czech Trade Inspection Authority collected 221 fuel samples to inspection of quality at filling stations. Two samples failed the requirement of technical standards – one diesel sample didn’t reach the limit determined for flash point and an Ethanol E85 sample failed concerning vapour pressure. Sale of almost 8,200 litres of these poor quality fuels amounting to more than CZK 200,000 was prohibited by a CTIA measure. The total ratio of 0.9 % of poor quality samples belongs to the results with the last year’s lowest ratio of findings – which is a good news especially for motorists.

During January, samples of petrol, diesel, LPG, CNG, and Ethanol E85 were collected to inspections of quality in compliance with the Act No. 311/2006 Coll. on Fuels, and the Decree No. 133/2010 Coll. on the Quality and Evidence of Fuels. 2 of 221 collected and inspected fuel samples failed determined quality requirements, i.e. 0.9%.

Diesel

In January, in total 104 diesel samples were collected, including one that failed the quality requirements of the applicable technical standard, namely concerning the indicator flash point. The measured value was 48.0°C while the minimal required value is 53.0°C when measurement uncertainty is taken into account. Other inspected and analysed diesel samples met the quality requirements determined by the technical standard ČSN EN 590(2014) – Automotive fuels – Diesel – Technical requirements and test methods.

Ethanol E 85

The only sample of Ethanol E85 collected to quality inspection failed the quality parameter vapour pressure. Laboratory analysis showed the value of 42.4 kPa while the minimal value is 48.0 kPa as determined by the technical standard ČSN P CEN/TS 15293 Automotive fuel – Ethanol E 85 - Technical requirements and test methods when measurement uncertainty is taken into account.

Organic ingredients in fuels

Content of fatty acid methyl ester was inspected concerning 104 diesel samples and ethanol content was inspected concerning 89 petrol samples. Violation of the upper acceptable limit of bio ingredients content wasn’t detected during the monitored period.

Measures

The Czech Trade Inspection Authority imposed prohibition on sale of fuels that failed the requirements of special legal regulations (pursuant to the provision of section 7 par. 1 letter a) of the Act No. 64/1986 Coll. on the CTIA). The prohibition was imposed on 5,552 litres of diesel amounting to CZK 146,017.60 and 2,636.79 l E-85 amounting to CZK 68,292.86.

Conclusion

Laboratory analysis of diesel fuel samples collected in January 2016 proved deviations from quality standards concerning one sample of diesel and one sample of E-85. When compared with results in December, the ratio of poor quality samples decreased by 0.8% (from 1.7% in December 2015 down to 0.9% in January 2016).

Results according to inspectorates

Legend: Coll = collected, N = noncompliant

Attachment: 	Monitoring of fuels quality in January 2016