|  | PRESS RELEASE |
| --- | --- |

SCOOTER Jrl 204033 is not safe

(Prague, April 6, 2016) In the spring time people start buying scooters especially for children. However, not all scooters are safe. This has been the case of a toy which was detected in the Czech market and which poses risk of injury to smallest users. The Czech Trade Inspection Authority ordered immediate withdrawal of the product from distribution. The product failed safety requirements within several parameters, namely concerning protruding parts, wheels and strength. The toy was notified as dangerous into the RAPEX database, notification number A12/0028/16.

Children’s folding scooter – SCOOTER Jrl 204033

Manufacturer:			unknown

Importer:			T-N, hračky domácí potřeby, s.r.o.

Name of the product:	 	Scooter

Name of the product (label): 	Skateboard - Koloběžka

Model: 				Item No. Jrl 204033

EAN (displayed on label):	6900012040336

Product description:		made in China

Picture No. 1 - Original product within sale

Product description

The particular folding scooter with one wheel in the front and two wheels at the rear can be red or green. Coloured motives of a rabbit with a crown are on the steering tube and the standing area. The toy is sold in a cardboard box which is red, white and blue. A different scooter model than the one that is folded inside is displayed on the upper part of the box.

Danger

The product failed requirements determined by the Government Order No. 86/2011 Coll. on Technical Requirements for Toys because it failed safety requirements that are laid down in detail in the applicable technical standard (ČSN EN 71-1:2011 + A3:2014):

- Black protective handlebar covers are removable without the necessity to use any power despite the minimum requirement is 60 N (Article 4.9 – Protruding parts);

- Diameter of the handle ends was 33 mm despite the minimal required proportion is 40 mm pursuant to Article 4.15.5.7 – Protruding parts);

Picture No. 2 – accessible wholes at the end of handles

- A stick of the diameter of 5 mm can be inserted to the gaps between the wheels and the toy’s body while a stick of the diameter of 12 mm cannot be inserted at the same time (pursuant to Article 4.15.1.6 – Transmission and wheel arrangement);

- During the strength test the steering tube with handlebar collapsed. The steering tube can also be separated into two parts. (Article 4.15.5.3 – Strength).

Picture No. 3 Collapsed steering tube

It is probable that within use of the product a dangerous situation can occur when a child user can get injured from the above mentioned reasons. The hazard concerns finger clash within manipulation with the scooter or a fall in the consequence of insufficient strength of the used material and mounting of the handlebar and its protective covers.

Taken measures

The Czech Trade Inspection Authority imposed a protective measure on the trader who was ordered to immediately withdraw the product from distribution in order to prevent further sale of the same products that fail the technical requirements for toys. All information about the dangerous scooter were published in the system RAPEX, notification number A12/0028/16.