|  | PRESS RELEASE |
| --- | --- |

Fuels quality slightly worsened in April

(Continuous report of April 2016)

(Prague, May 25, 2016) In April the Czech Trade Inspection Authority collected 224 fuel samples at filling stations. Four of them failed the quality requirements determined by applicable technical standards. Slight quality decrease was seen in comparison with March 2016, namely from 1.5% to 1.8%. So called negligence deviations were proven concerning two diesel samples, one diesel fuel blend sample and one FAME sample. Noncompliance with the applicable standard was detected concerning flash point in all the cases. Noncompliance with the determined limit for flash point signals contamination of fuels with an unfavourable admixture, e.g. automotive petrol in case of diesel. Prohibition of sale of fuels that failed requirements of special legal regulations was imposed in two cases in April, namely on 9,071.9 litres of fuels amounting to CZK 213,062.

Monitoring of fuel quality is carried out in compliance with the Act No. 311/2006 Coll. on Fuels and the Decree No. 133P2010 Coll. on the Quality and Evidence of Fuels, at filling stations on the whole territory of the Czech Republic. In April 2015 samples of automotive petrol, diesel, diesel fuel blend, bio fuel, LPG, CNG and Ethanol E85 were collected to inspections.

Inspection results

In April, 4 of 224 collected samples failed the quality requirements, i.e. 1.8%.

Diesel

In April, 103 diesel samples were collected, including 2 samples that failed the technical requirements of the applicable technical standard. Both inspected samples failed the quality requirements for flash point. The value of this quality parameter was 44.5°C, the value was 46.5°C concerning the other sample. The minimal value is 53°C when measurement uncertainty is taken into account as stipulated in the technical standard ČSN EN 590(2014) – Motor Fuels – Diesel – Technical Requirements and Test Methods. All the other fuel diesel samples met the requirements of the technical standard.

Diesel fuel blend

2 samples of diesel fuel blend (DBF 30) were collected, including one that failed the quality parameter flash point. The measured value was 20.5°C despite the minimal value shall be 53.0°C as required by the applicable technical standard. Fuel with such low value of flash point poses a risk of engine damages. The other inspected sample met the quality requirements of the standard ČSN 65 6508(2013) – Motor fuels – Diesel fuel blend containing fatty acid methyl ester (FAME) – Technical Requirements and Test Methods.

FAME

1 of 4 collected and inspected FAME samples failed. Deviation was detected concerning the quality parameter flash point. Minimal value is 94.5°C when measurement uncertainty is taken into account despite the flash point of the measured sample was 78.0°C. Other FAME samples met the requirements of the applicable technical standard ČSN EN 14214+A1(2014) Liquid petroleum products – Fatty acid methyl esters (FAME) for use in diesel engines and heating applications – Technical Requirements and Test Methods.

Bio ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected concerning 103 diesel samples and 88 automotive petrol samples. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored fuel types.

Imposed measure

In April, the Czech Trade Inspection Authority imposed measures consisting of prohibition of sale of fuels that didn’t comply with the requirements of special legal regulations in 2 cases. The measure was issued on 9,071.9 litres of fuels amounting to CZK 213,062.21, namely on 1,771.9 litres of diesel fuel blend amounting to CZK 45,892.21 and 7,300 litres of FAME amounting to CZK 167,170.

Conclusion

Laboratory analysis of collected fuel samples showed deviations from quality standards in two diesel samples, one diesel fuel blend sample and one sample of FAME. Quality decrease was seen concerning diesel fuel blend and FAME, on the contrary the ratio of poor quality diesel fuel samples decreased in comparison with March 2016. In total the ratio of poor quality samples decreased from 1.5% to 1.8% in April 2016.

Results according to inspectorates

Legend: Coll = collected, N = noncompliant

Attachments: 	Monitoring of fuels quality in April 2016

Monitoring of fuels quality from January to April 2016