|  | PRESS RELEASE |
| --- | --- |

Playpen BABY VIVO doesn’t secure safety

(Prague, August 23, 2016) During inspections of products intended for children, the Czech Trade Inspection Authority discovered that a playpen BABY VIVO which poses serious safety risk to smallest users is offered in the market. There is a risk of finger entrapment or damage because when opening the gate a cutting place occurs in the area of the hinge. The Czech Trade Inspection Authority ordered immediate withdrawal of the product from distribution. Complete documentation concerning the dangerous playpen was handed over to the RAPEX contact point and published in the database under the notification number A11/0061/16.

Product description

A classic 8-piece timber playpen with a gate made of timber of natural colour. The playpen can be constructed in several shapes. The door is equipped with safety lock. Instructions for use are labelled with the CE marking which is in contradiction with the applicable regulations.

Playpen – BABY VIVO

Identification date of the product:

Contact details of the distributor:	MA Trading GmbH & Co. KG, Nimrodstr. 9,

90441 Nümberg

Product name: 				BABY VIVO

Model:                                    		SL 130 B

Production series number:		ID 34534523

Original product packaging

Danger

- Fingers can get trapped. In the lower part of the gate are two places where a probe of ø 7 mm goes to the depth of minimally 10 mm and at the same time the probe of ø 12 mm can’t go through. The mentioned probes represent children’s fingers.

- Cutting part can be identified in the area of the hinge. Gate parts don’t get as close as 12 mm when fully opening the door and, hence, the cutting place.

Cutting place identified in the test room

It is possible that within a common and predictable use of the product a situation occurs during closing and opening the gate when child’s fingers can be injured if put into the cutting place between the gate and the playpen. A child can also insert its finger into the occurred space in the below part of the gate.

Conclusion

Expert assessment showed that the classic timber playpen doesn’t meet the requirements of the Act No. 102/2001 Coll. on General Safety of Products. Within tests carried out according to the requirements of the applicable European standard ČSN EN 12227 in a laboratory, numerous defects with significant influence on the safety of the particular product were detected.

Taken measures

The Czech Trade Inspection Authority imposed the inspected entity, i.e. the final distributor of the playpen, a protective measure to immediately withdraw the product from the distribution. All available document and information about the dangerous playpen BABY VIVO were handed over to the contact point at the MIT and subsequently published in the pan-European database RAPEX, notification number A11/0061/16.