|  | PRESS RELEASE |
| --- | --- |

CTIA found 3 noncompliant fuel samples in September

(Prague, October 26, 2016) In September, the Czech Trade Inspection Authority carried out regular sampling and inspections of fuels. Three of 215 fuel samples failed the quality requirements, hence, the situation slightly worsened when compared with August. Prohibition of sale was imposed on more than 6,500 litres of fuels amounting to almost CZK 151,000.

In September, the Czech Trade Inspection Authority monitored the quality of fuels at filling stations on the whole territory of the Czech Republic. Automotive petrol, diesel, LPG, CNG, and Ethanol E85 were inspected through sampling and laboratory analysis.

In September, 3 of 215 inspected fuel samples failed the quality requirements which stands for 1.4%. The Czech Trade Inspection Authority imposed prohibition on sale of 4,256.2 litres of petrol amounting to CZK 122,599.29 and 2,247 litres of LPG for engines amounting to CTK 27,862.80.

Petrol

In September 2016, the Czech Trade Inspection Authority collected and inspected 81 samples of automotive petrol, including one sample which failed the quality requirements determined by the applicable technical standard. The inspected sample failed the quality indicator “vapour pressure”. The measured value of the quality parameter was 78.5 kPa while the maximal value id 62.0 kPa when measurement uncertainty is taken into account.

Diesel

In the monitored period, the Czech Trade Inspection Authority collected and inspected 106 samples of diesel, including one which failed the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter “Flash point”. The value 47.5°C was measured within this sample while the minimum value is 53.0°C when measurement uncertainty is taken into account.

LPG for engine

The Czech Trade Inspection Authority collected and inspected 74 LPG samples, including one which failed the requirements of the applicable technical standard. The sample failed the quality parameter “Sulphur”. The measured value was 96.0 mg/kg while the maximum value is 71.0 mg/kg when measurement uncertainty is taken into account.

Organic fuels in fuels

In the monitored period, content of fatty acid methyl ester was inspected within 106 samples of diesel. Ethanol content in automotive petrol was inspected in 81 cases. Violation of the upper acceptable level of organic ingredients wasn’t detected in the exercised motor fuels within laboratory analysis.

Conclusion

When compared with August, 2016, the quality of inspected petrol samples worsened from 0.0% to 1.2% and LPG samples from 0.0% to 4.2%. Ratio of poor quality diesel samples remained on 0.9%. The overall quality of sampled fuels decreased from 0.4% to 1.4% in September, 2016, when compared with August, 2016. Samples of diesel fuel blend (DFB 30) and FAME were not collected in September.

Legend: COLL = collected, N = noncompliant