|  | PRESS RELEASE |
| --- | --- |

January fuel inspection saw 1 noncompliant sample

(Praha, March 1, 2017) The Czech Trade Inspection Authority has continued its inspections of fuels in 2017. One of 226 samples collected in January failed the quality requirements. There was a slight decrease regarding the quality of sampled fuels from 0.0% to 0.4% in comparison with December 2016 when no poor quality sample was proven in laboratory analysis.

The Czech Trade Inspection Authority regularly monitors the fuels quality at filling stations on the territory of the Czech Republic. In January 2017 it took 226 fuel samples, including one that failed the quality requirements, which represented 0.4% of noncompliant samples.

Diesel

In January 2017, the Czech Trade Inspection Authority took and inspected 106 diesel samples, including one that failed the quality requirements. The inspected sample failed the quality parameter “Flash point”. The measured value was 50.0°C while the minimal value shall be 53.0% when measurement uncertainty is taken into account. The remaining inspected and analysed diesel samples met the quality parameters determined by the technical standard ČSN EN 590 – Motor Fuels – Diesel – Technical Requirements and Test Methods.

Bio ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected concerning 106 diesel samples. Ethanol content was inspected concerning 88 automotive petrol samples. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored fuel types.

CONCLUSION

Laboratory analysis of the sampled fuels proved deviations from quality standards in one diesel sample. Samples of diesel fuel blend DFB 30, FAME and the fuel E 85 weren’t taken in January 2017. The overall evaluation and comparison of the quality of sampled fuels showed slight decrease in the ratio of poor quality samples – from 0.0% to 0.4%.

Results according to individual inspectorates

Legend: Coll = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring of fuels quality in March 2016 (2 pages)

No. 2. – Noncompliant samples – January 2017 (1 page)