|  | PRESS RELEASE |
| --- | --- |

CTIA found three noncompliant fuel samples in February

(Prague, April 5, 2017) The Czech Trade Inspection Authority continues its inspections of fuel quality in 2017. In February, it carried out takings of 211 samples, including three that failed the quality requirements. In comparison with January 2017 a slight decrease regarding quality was observed from 0.4% to 1.4%. Prohibition of sale was imposed on more than 19,000 litres of diesel amounting to almost CZK 480,000.

In February 2017, CTIA officers carried out 211 takings of fuel samples at filling stations on the whole territory of the Czech Republic. Three samples failed the quality requirements which represented 1.4% of noncompliant samples.

The aim of the CTIA monitoring was the inspection and monitoring of the quality of petrol, diesel, LPG, CNG, and Ethanol E85 carried out by fuel sampling and laboratory analysis. Officers inspected compliance with the provision of section 3 par. 1 of the Act No. 311/2006 Coll. on Fuels and Filling Stations. Laboratory analysis of fuel samples proved deviations from quality standards in one diesel sample, one petrol sample and one sample of Ethanol E 85.

In comparison with January 2017, decrease regarding the quality of collected diesel samples was observed from 0.9% to 1.0% as was in case of petrol from 0.0% to 1.2%. Results of the E85 cannot be compared because in January 2017 no samples were taken.

The overall evaluation showed that the quality of taken fuel samples worsened from 0.4% to 1.4% in February 2017 when compared with February 2017.

Petrol

In February 2017, the Czech Trade Inspection Authority took and inspected 83 petrol samples, including one that failed the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter “Distillation test – end of distillation”. The measured value was 224.2°C while the maximal value shall be 214.0% when measurement uncertainty is taken into account. The remaining inspected and analysed petrol samples met the quality parameters determined by the technical standard ČSN EN 228 (2013) – Motor Fuels – Unleaded Petrol – Technical Requirements and Test Methods.

Diesel

In February 2017, the Czech Trade Inspection Authority took and inspected 99 diesel samples, including one that failed the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter “Flash point”. The measured value was 49.0°C while the minimal value shall be 53.0% when measurement uncertainty is taken into account. The remaining inspected and analysed diesel samples met the quality parameters determined by the technical standard ČSN EN 590 – Motor Fuels – Diesel – Technical Requirements and Test Methods.

Ethanol E 85

In February 2017, the Czech Trade Inspection Authority took and inspected 2 samples of this fuel type and laboratory analysis showed the value of 44.0 kPa while the minimal value shall be 48.0 kPa when measurement uncertainty is taken into account. The other inspected and tested samples met the quality parameters determined by the technical standard ČSN P CEN/TS 15293– Motor Fuels – Ethanol E 85 – Technical Requirements and Test Methods.

Organic ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected concerning 99 diesel samples. Ethanol content was inspected concerning 83 automotive petrol samples. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored fuel types.

Imposed measures

In February 2017, the Czech Trade Inspection Authority imposed prohibition on sale of fuels that failed the requirements for quality and composition as determined in the implementing legal regulation, special legal regulations and Czech technical standards.

The measure was imposed on 13,047.69 litres of Ethanol E 85 amounting to CZK 298.792.10, and 5,997.50 litres of diesel amounting to CZK 181,124.50.

Results according to inspectorates

Legend: Coll = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring of fuels quality in March 2016 (2 pages)

No. 2. – Noncompliant samples – January 2017 (2 pages)