|  | PRESS RELEASE |
| --- | --- |

July – major improvement of sampled fuels quality

(Prague, August 30, 2017) The Czech Trade Inspection Authority saw a major increase of sampled fuels quality in July when compared with June 2017 – the increase was by almost 2.5%. Only two diesel samples failed.

The Czech Trade Inspection Authority monitors the quality of fuels on the territory of the Czech Republic pursuant to the Act No. 311/2006 Coll. on Fuels and Decree No. 133/2010 Coll. on Quality and Records of Fuels. Fuels are inspected at filling stations on the whole territory of the Czech Republic.

In July, the Czech Trade Inspection Authority collected 212 fuel samples. 2 collected and inspected samples failed the quality requirements and, thus, represented 0.9% of noncompliant samples.

The Czech Trade Inspection Authority saw a significant increase in the quality of sampled automotive petrol from 7.4% to 0.0%. Diesel worsened from 0.8% to 2.0%. DFB 30, FAME, and Ethanol E 85 weren’t sampled in July 2017.

Inspectors saw the increase in quality of fuel samples by almost 2.5%, namely from 3.3% to 0.9% in comparison between June and July 2017.

In one case, the Czech Trade Inspection Authority imposed prohibition on sale of 10,330.36 litres of diesel in the value of CZK 298,547.40.

Diesel

In the monitored period, the Czech Trade Inspection Authority collected in total 101 diesel samples, including two that failed the quality requirements of the applicable technical standard. In one case, the inspected diesel sample failed the quality parameter “Flash point” – measured value was 50.0°C while the minimal value is 53.0°C when measurement uncertainty is taken into account. Laboratory analysis showed that the maximal acceptable limit of sulphur content was exceeded – the measured value was 26.1 mg/kg while the maximal value Is 12.0 mg/kg when measurement uncertainty is taken into account.

The other inspected and analysed diesel sample met the quality requirements as stipulated in the technical standard ČSN EN 590 (2014) – Motor fuels – Diesel – Technical requirements and test methods.

Organic ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected in 101 diesel samples. Ethanol content was inspected in 84 petrol samples. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored fuel types.

Results according to inspectorates

Legend: COLL = collected, N = noncompliant

Attachments:

No. 1 - Monitoring of fuels quality – July 2017

No. 2 - Monitoring of fuels quality – January to July 2017