|  | PRESS RELEASE |
| --- | --- |

2 diesel samples failed in December

(Prague, February 22, 2018) In December 2017, the Czech Trade Inspection Authority inspected fuels quality at filling stations. From the total number of 179 taken samples, two diesel samples failed the requirements.

The Czech Trade Inspection Authority regularly monitors fuels quality at filling stations on the whole territory of the Czech Republic. Inspection is carried out by sampling and laboratory analysis. In December 2017, CTIA took 179 fuel samples, including two diesel samples that failed the quality requirements.

In comparison with November 2017, there was a quality decline from 0.8% to 1.1% within the overall assessment and comparison of the quality of sampled fuels in December 2017.

Diesel

In December 2017, the Czech Trade Inspection Authority collected and inspected in total 88 diesel samples, including 2 samples that failed the quality requirements governed by the applicable technical standard. Inspected diesel samples failed the quality parameter “Flash point” – the measured values were 45.5°C and 46.5°C while the minimum value is 53.0°C when measurement uncertainty is taken into account. The remaining inspected and analysed diesel samples failed the quality parameter stipulated in the technical standard ČSN EN 590(2014) – Motor Fuels - Diesel – Technical Requirements and Test Methods.

Organic fuels

In the monitored period, content of fatty acid methyl ester was inspected in 88 diesel samples and ethanol content was inspected in 70 samples of automotive petrol. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored fuel types.

Fuel inspections results according to inspectorates

Legend: COLL = collected, N = noncompliant