|  | PRESS RELEASE |
| --- | --- |

Children’s dangerous toy „Mini Kitty“

(Prague, February 1, 2018) The Czech Trade Inspection Authority detected that a toy is offered in the Czech market which can pose serious health risk to children. It is a meowing bag „Mini Kitty in the Bag“.

During regular inspections, the Czech Trade Inspection Authority detected that vendors offer and sell a toy with parameters that fail technical standards. It is a softly filled bag made from a coarse burlap that makes sound similar to cat’s meowing after it is pushed. A plastic pink carbine to hang is sewed to the bag whose upper edges are pulled by a yarn. A piece of plush with brown and black stripes is sewed on the side, imitating a tail or a paw. Long brown fibres, imitating fur, hang from the sacking at two randomly selected places. An unintelligible text and a “logo” are printed on the bag to which a paper label is affixed, displaying the product name „Mini Kitty Bag“, and the marking „Keychain“. A CE marking in an incorrect shape as well as the symbol “Unsuitable for children under three years” with no indication of reason to such marking, are on the reverse side of the label. English information that the toy contains three button batteries is displayed on the label.

CTIA inspections identified the causes of danger. The pulling yarn can easily go through the coarse burlap although nodes are on the yarn ends. So, the bag can be opened easily and a fibre material and a plastic box with a loud-speaker can be found inside. The box can be opened and button batteries can be taken out. The product is not in compliance with legal regulations on safety of electric toys. Button batteries are easily removable from the toy without the necessity to use any tool. The cover can be opened by one move. The batteries can be put into mouth and swallow or inhale.

CTIA ordered immediate withdrawal of all toys „Mini Kitty in the Bag“ from distribution. Information about the toy was also notified to the contact point at the Ministry of Industry and Trade and published in the alert system for dangerous products RAPEX.

Fotografie výrobku v nabídce

Otevřený pytlík a krabička se zvukovým mechanizmem a s nezajištěným prostorem pro baterie.

Mňoukací pytlík „Mini Kitty in the Bag“

Název výrobku:				„Mini Kitty in the Bag“ KEYCHAIN

Typ / číslo modelu:			Item No: 520

Země původu hračky:			made in China

Identifikační údaje výrobce:	neuvedeno

Identifikační údaje distributora:		neuvedeno

Prodejce:				Duy Son Tran, Náměstí 19, 542 42 Pilníkov