|  | PRESS RELEASE |
| --- | --- |

One diesel sample filed in January

(Prague, March 14, 2018) The Czech Trade Inspection Authority inspected fuels quality in January 2018. Only one sample failed the quality requirements. It was a diesel sample.

The Czech Trade Inspection Authority monitored the quality of fuels at filling stations on the whole territory of the Czech Republic in January 2018. Inspection and monitoring of samples of automotive petrol, diesel, LPG, CNG, and Ethanol E85 were carried out by sampling and laboratory analysis. DFB 30 and FAME weren’t sampled in January 2018 with regard to the development in the fuels market.

In January 2018, one diesel sample of all 215 collected fuel samples failed the quality requirements.

When compared with December 2017, there was an improvement in cases of sampled fuels. In December 2017, two diesel samples failed the quality requirements.

Diesel

In January 2018, the Czech Trade Inspection Authority took and inspected in total 105 diesel samples, including 1 sample that failed the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter “Flash point” – the measured value was 48.5°C while the minimum value is 53.0°C required when measurement uncertainty is taken into account. The other inspected and analysed diesel samples met the quality requirements governed by the technical standard ČSN EN 590(2014) – Motor Fuels - Diesel – Technical Requirements and Test Methods.

Organic ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected in 105 diesel samples and ethanol content was inspected in 82 samples of automotive petrol. Laboratory analysis didn’t show any violation of the upper acceptable level of bio ingredients in samples of the monitored motor fuel types.

Fuel inspections results according to inspectorates

Legend: COLL = collected, N = noncompliant

Attachment: No. 1 - Monitoring of fuels quality in January 2018