|  | PRESS RELEASE |
| --- | --- |

CTIA monitored fuels quality in February 2018

(Prague, April 19, 2018) The Czech Trade Inspection Authority carried out fuels quality inspections in February 2018. Out of the total number of 217 sampled fuels, two diesel samples failed the quality requirements.

The Czech Trade Inspection Authority carries out regular monitoring of fuels quality (automotive petrol, diesel, diesel fuel blend, organic fuels, LPG, CNG, and Ethanol E85) at filling stations on the whole territory of the Czech Republic. With regard to the development in the fuels market, samples of DSB 30 and FAME weren’t collected in February 2018. The inspection was carried out through fuels sampling and laboratory analysis.

The Czech Trade Inspection Authority saw failures to meet the requirements in two cases – both concerned diesel samples. It was a worse result than in January when one diesel sample failed.

Diesel

In February 2018, the Czech Trade Inspection Authority collected and inspected in total 107 diesel samples, including two samples that failed the quality requirements of the applicable technical standard. Inspected samples failed the quality indicator “Flash point” – the measured value was 46.5°C in one case and 52.0°C in the other, while the minimal required value is 53.0°C when measurement uncertainty is taken into account. The other inspected and analysed diesel samples met the requirements set by the technical standard ČSN EN 590(2014) – Motor Fuels - Diesel – Technical Requirements and Test Methods.

Organic ingredients in fuels

In the monitored period, content of fatty acid methyl ester was inspected within 107 diesel samples. Ethanol content was inspected within 82 petrol samples. Laboratory analysis showed that the upper acceptable limit of the content of organic ingredients was exceeded within the monitored motor fuels.

Measures

In February 2018, the Czech Trade Inspection Authority imposed measures consisting of the prohibition to sell fuels in two cases – the fuel samples failed the requirements for quality and composition as governed by a legal regulation as well as Czech technical standards. The measure was imposed on 4,919.14 litres of diesel in the value of CZK 147,064.50.

Inspection results according to individual inspectorates:

Legend: COLL = collected, N = non-compliant

Attachments:

No. 1 - Monitoring of fuels quality – February 2018

No. 2 - Monitoring of fuels quality – January and February 2018