|  | PRESS RELEASE |
| --- | --- |

A diesel fuel sample failed in April

(Prague, May 31, 2018) The Czech Trade Inspection Authority found a noncompliant fuel sample in April. It was a diesel sample.

The Czech Trade Inspection Authority monitored the quality of fuels in the Czech Republic in April 2018. Inspection and monitoring were carried out by sampling and laboratory analysis.

Out of 211 samples taken, 1 diesel fuel sample didn‘t meet the specified quality requirements within the inspection of fuels.

Diesel

A total of 105 diesel fuel samples were taken and inspected by the Czech Trade Inspection Authority in April 2018. 1 sample didn‘t meet the quality requirements of the applicable technical standard. The tested diesel fuel sample didn‘t meet the quality parameter “Flash point” because the measured value of this quality parameter was 51.5°C (the minimum value is 53.0 ° C when the measurement uncertainty is taken into account). The remaining inspected and analysed samples of diesel fuel met the quality requirements set out in the technical standard ČSN EN 590 + A1 - Motor Fuels - Diesel Fuel - Technical Requirements and Test Methods.

Organic ingredients in fuels

Content of fatty acid methyl ester was inspected within 105 diesel samples in the monitored period. Ethanol content was inspected within 79 petrol samples. Laboratory analysis showed that the upper acceptable limit of the content of organic ingredients wasn’t exceeded within the monitored motor fuels.

Inspection results according to individual inspectorates:

Legend: COLL = collected, N = non-compliant

Attachments:

No. 1 - Monitoring of fuels quality – April 2018

No. 2 - Monitoring of fuels quality – January and April 2018