|  | PRESS RELEASE |
| --- | --- |

Two fuel samples failed in September

(Prague, October 31, 2018) The Czech Trade Inspection Authority monitored the fuel quality in September 2018. It took 226 fuel samples at filling stations, including 2 samples that failed the quality requirements.

The Czech Trade Inspection Authority monitors the quality of motor fuels. The inspection is carried out in the form of sampling and laboratory analysis. In September 2018, 226 fuel samples were collected and 2 diesel samples failed the quality requirements. Compared to August, there were improvements in September, as 4 samples (3 samples of automotive petrol and 1 diesel sample) failed in August.

Diesel

In September 2018, the Czech Trade Inspection Authority took and inspected the total of 110 diesel fuel samples. 2 of these samples didn’t meet the quality requirements of the relevant technical standard. The inspected diesel fuel samples failed to meet the quality parameter “Sulphur”, where the measured value of this quality parameter was 89.0 mg/kg for the first sample. The other sample, which was a verification sample, showed the sulphur content of 23.7 mg/kg while the maximum value is 12.0 mg/kg when the measurement uncertainty is taken into account. The remaining inspected and analysed samples of diesel fuel met the quality parameters as set in the technical standard ČSN EN 590 + A1 – Motor fuels – Diesel fuel – Technical Requirements and Test Methods.

Organic ingredients in fuels

The content of fatty acid methyl ester was inspected in 110 diesel samples. Ethanol content was inspected in 86 petrol samples. Laboratory analysis showed no violation of the upper acceptable limit of organic ingredients in the collected samples of monitored automotive fuels.

Results of inspections focused on fuels quality – according to individual inspectorates:

Legend: C = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring of fuels quality - September 2018

No. 2 - Monitoring of fuels quality from January to September 2018