|  | PRESS RELEASE |
| --- | --- |

2 fuel samples failed in November

(Prague, December 31, 2018) In November 2018, the Czech Trade Inspection Authority took in total 255 fuel samples at filling stations. Deviations from the quality standards were proven in cases of two samples, including automotive petrol and diesel. When compared with October 2018, the quality worsened from 0.0% to 0.8% regarding diesel samples and from 0.0% to 1.1% in case of automotive petrol. Samples of DFB 30 and FAME weren’t collected in November 2018.

During November 2018, inspectors of the Czech Trade Inspection Authority sampled automotive petrol, diesel, diesel fuel blend, organic fuel, LPG, CNG, and Ethanol E85 within the yearlong monitoring of fuels quality on the whole territory of the Czech Republic, based on the provision of section 7 par 2 letter a) of the Act No. 311/2006 Coll. On Fuels, and the Decree No. 133/2010 Coll. on the Quality and Evidence of Fuels (further on referred to as Decree).

Inspection results

Out of the total number of 255 fuel samples collected and inspected in November 2018, two inspected samples failed the quality requirements, which represented 0.8% of noncompliant samples.

- Automotive petrol

The Czech Trade Inspection Authority collected and inspected in total 91 samples of automotive petrol, including 1 sample that failed the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter “Induction period” (long-term stability parameter of the gasoline when it is being exposed to oxygen) – the measured value was 287 minutes (minimal value is 339 minutes when measurement uncertainty is taken into account). Other inspected and analysed samples of automotive petrol met the quality requirements as stipulated by the technical standard ČSN EN 228+A1 – Motor Fuels – Unleaded Automotive Petrol – Technical Requirements and Test methods.

- Diesel

In November 2018, the Czech Trade Inspection Authority collected and inspected in total 128 diesel samples, including 1 analysed and inspected sample that failed the quality requirements of the applicable technical standard. The inspected diesel sample failed the quality parameter “Temperature of filterability” – the measured value of this quality parameter was -5°C while the maximal value is -8°C when measurement uncertainty is taken into account. The other inspected and analysed samples of diesel met the quality requirements stipulated in the technical standard ČSN EN 590+A1 – Motor Fuels - Diesel – Technical Requirements and Test Methods.

- Organic ingredients in fuels

The content of fatty acid methyl ester was inspected in 128 diesel samples. Ethanol content was inspected in 91 petrol samples. Laboratory analysis showed no violation of the upper acceptable limit of organic ingredients in the collected samples of monitored automotive fuels.

Conclusion

When compared with October 2018, in November 2018 the quality of collected fuel samples worsened from 0.0% to 0.8% in case of automotive petrol and from 0.0% to 1.1% in case of automotive petrol. Samples of DNB 30 and FAME weren’t collected in November 2018.

Out of the total number of 255 fuel samples collected and inspected in November 2018, two inspected samples failed the quality requirements, which represented 0.8% of noncompliant samples.

Results of inspections focused on fuels quality – according to individual inspectorates:

Legend: COLL = collected, N = non-compliant

Attachments:

No. 1 - Monitoring of fuels quality – October 2018

No. 2 - Monitoring of fuels quality – January and October 2018