|  | PRESS RELEASE |
| --- | --- |

Mobile charger „PDFVJB“ is also dangerous

(Prague, August 7, 2019) The Czech Trade Inspection Authority warns consumers against another dangerous mobile phone charger on which the text “4-OK” is displayed as is its name „PDFVJB“. The inspection detected a serious risk of injury by electric current.

The following text is displayed on the product: Input: 100-240V ~ 50/60Hz 0,15A, Output: 5.0V = , 1A, CE marking and the sign of the protection class II, Made in China. The following text is displayed on the packaging: NPDFVJB 4-OK PACK CABLE DATAFLAT WHITE + TRAVEL-HOME CHARGER-1 AMP USB WHITE. A USB package of USB 230V charger with the maximum of 1AMP on the output and a data cable USB/micro USB (which can also be used for charging the device) is a part of the product. Further it is stated that the product was produced in China, EAN 8 428728 060922, Distributor: GameAD, s.r.o., Kostelecká 879/59, Praha, 19600.

The CTIA warns against a high safety risk. When using the product, insufficient isolation between the primary and secondary parts of the product may be broken, and the dangerous 230V voltage from the primary part could get to the USB connector in the secondary part. If the user touches the connector when the charger is plugged in, the situation can result in a serious injury or even death due to the electric shock. In addition, identification data of the manufacturer aren’t displayed on the packaging.

The Czech Trade Inspection Authority imposed a protective measure consisting of the prohibition to supply the product to the market and the withdrawal of the product from the market. The product was notified to the RAPEX contact point at the Ministry of Industry and Trade and the information will be published in the RAPEX system.

Picture of the packaging and the product within the offer

Product information

Product name: 		Mobile phone charger

Model type / number:	PDFVJB 1A

Product number/EAN:	8428728060922

Identification data about the manufacturer:      Blautel (Shuttle&Blautel) S.L. –CIF.:B61529634, C/Cargol, 13 NAVE 10, Poligono Industrial Coll de Montcada 08110 Montcada i Reixac (Barcelona)

Identification data about the importer:	-

Distributor:	HP TRONIC Zlín spol. s r.o., Kútiky 637, 76001 Zlín-Prštné

Country of origin: 	China