|  | PRESS RELEASE |
| --- | --- |

CTIA prohibited fifth mobile phone charger in the market

(Praha, August 14, 2019) The Czech Trade Inspection Authority found out that a mobile phone charger “EKA-Q27 USB Hybrid Charger” was offered in the domestic market, which could pose a serious safety risk for consumers due to electric shock it could cause.

The mobile phone charger EKA-Q27 USB Hybrid Charger TC E250 is in a plastic packaging. The following text is displayed on the product: AC adapter P/N: 79H00098-02M, CE marking, model TC E250, Input 100-240V, 50-60Hz, Output 5V, 2000mA, sign of the protection class II, made in China, marking for indoor use, and the sign of separate waste. The following information is displayed on the packaging: 110-220V AC Power source, Car Charger 12-24V DC Power source, 5-5,5V DC output, Max 2100mA output. The following information is displayed on the sticker: VTV 3314-80, mobile accessories, country of origin P.R.C. (Peoples Republic of China), importer to the Czech Republic TV MAX market s.r.o., ul. Tiškarská, Praha 10, EAN 8177183314803.

Laboratory tests proved a high safety risk. When using the product, insufficient isolation between the primary and secondary parts of the product may be broken, and the dangerous 230V voltage from the primary part could get to the USB connector in the secondary part. If the user touches the connector when the charger is plugged in, the situation can result in a serious injury or even death due to the electric shock. In addition, identification data of the manufacturer aren’t displayed on the packaging.

The Czech Trade Inspection Authority imposed a protective measure consisting of the prohibition to supply the product to the market and the withdrawal of the product from the market. The product was notified to the RAPEX contact point at the Ministry of Industry and Trade and the information will be published in the RAPEX system.

Picture of the packaging and the product in the offer

Product information

Mobile phone charger EKA-Q27 USB Hybrid Charger

Product name: 		Mobile phone charger

Model type / number: 	EKA-Q27 USB Hybrid Charger TC E250

Product number/EAN:	8177183314803

Identification data about the manufacturer: undetected

Identification data about the importer: TV MAX market s.r.o., ul. Tiškarská, Praha 10

Distributor:  MAXIHIT Liberec s.r.o., Dr. M. Horákové 585/92, 460 07 Liberec

Country of origin: China