|  | PRESS RELEASE |
| --- | --- |

One in ten inspected charging stations fully complied

(Final report of 2019)

(Prague, February 19, 2020) The Czech Trade Inspection Authority carried out a national inspection project focused on electric vehicle charging stations. The audited entities were distributors, importers and manufacturers of these products as well as authorised representatives. CTIA inspected 32 product types during 2019 and found deficiencies in 29 types.

In 2019, the Czech Trade Inspection Authority followed up on a pilot project of inspections of charging stations, carried out as early as 2018. As the popularity of electric vehicles and consumer interest in this type of product grows, the first national inspection project focused on this type of product took place last year.

CTIA inspectors verified the marking and labelling of products and the fulfilment of administrative requirements for the marketing and subsequent operation of these products. In the case of inspected operators, 50% were electricity distributors (ČEZ a.s., EON a.s., PRE a.s.), in 2 cases it was the chain store LIDL, v.o.s., and others were smaller Czech private companies. The operators are also owners of charging stations. As far as the manufacturers of these stations are concerned, 60% are large, eu-based foreign companies such as ABB, Schneider and Siemens, 20% of the Czech company - ČEZ a.s., PRE a.s., smaller companies, and 20% smaller foreign companies.

In total, the Czech Trade Inspection Authority inspected 32 types of products. In all cases, it was the so-called "green belt", high-performance charging stations with installed electric power of at least 22kW. It identified administrative deficiencies in 29 types. In 21 cases, there were shortcomings in information obligations – there were no instructions for use in the Czech language and failure to inform about the price. 7 products lacked the mandatory CE marking of conformity and 3 products weren’t equipped with contact details of the manufacturer, such as the name or the business name or a trademark, and the delivery address at which the vendor can be contacted. The identified deficiencies are addressed with manufacturers or the importers of these products within the surveillance authorizations of the CTIA.

The Czech Trade Inspection Authority imposed 6 fines amounting to CZK 67,000 for the infringements.

_______________________________________________________________________

Applicable legal regulations:

Government Order No. 117/2016 on conformity assessment of products in terms of electromagnetic compatibility, when placed on the market

Government Order No. 481/2012 Coll., on the Restriction of the Use of Certain Hazardous Substances in Electrical and Electronic Equipment

Government Order No. 481/2012 Coll., on the Restriction of the Use of Certain Hazardous Substances in Electrical and Electronic Equipment (Directive RoHS 2011/65/EU) and the Act No. 22/1997 Coll. on Technical Requirements for Products;

Act No. 90/2016 Coll., on conformity assessment of specified products when made available on the market, as amended

Furthermore, in cooperation with the administrative surveillance authorities (locally competent building authorities or department) fulfilling the obligations of the operator pursuant to Section 6q of the Act No. 311/2006 Coll., on Fuel and Filling Stations.

Conditions for the production and operation of public charging stations are laid down in harmonised standards:

ČSN EN 61851-1 ed.2 System of charging electric vehicles by conductive connection - Part 1: General requirements

ČSN EN 61851-21 Conductive interconnection charging system - Part 21: Electric vehicle requirements for conductive connection to an AC /DC supply

ČSN EN 61851-21-1 Conductive connection charging system - Part 21-1: Electric vehicle on-board charger EMC requirements for conductive connection to an AC/DC supply

ČSN EN 61851-22 System of charging electric vehicles by conductive connection - Part 22: AC charging station of electric vehicle

ČSN EN 61851-23 System of charging electric vehicles by conductive connection - Part 23: DC charging station

## ČSN EN 61851-24 Electric vehicle conductive charging system. Digital communication between a d.c. EV charging station and an electric vehicle for control of d.c. charging

## ČSN P ISO/TS 21219-25 Intelligent transport systems - Intelligent transport systems — Traffic and travel information (TTI) via transport protocol experts group, generation 2 (TPEG2) — Part 25: Electromobility charging infrastructure (TPEG2-EMI)