|  | PRESS RELEASE |
| --- | --- |

CTIA prohibited the toy „Doll Carrier“

(Prague, June 26, 2020) The Czech Trade Inspection Authority keeps monitoring possible occurrence of dangerous toys in the internal market. This time it found that a toys was offered posing a safety risk to smallest children. This product’s name is „Doll Carrier“.

The Czech Trade Inspection Authority found a dangerous toy on the market. It is a stroller "golf buggy", made of metal pipes with a pink surface. The seat is made of pink fabric with a printed motif of various teddy bears. Additional components of the stroller design, such as handles and wheels, are made of pink and white plastic. The product is packed in a plastic bag, which is closed with a paper label. The manufacturer marked and labelled the toy as unsuitable for children under three years of age due to possible suffocation after inhaling small parts.

In the accredited laboratory, it was found that the ends of the protruding parts of the seat structure have no protective components (see photo). In laboratory tests of the folding mechanism, it was found that the toy could be partially decomposed without the locking device being closed and that after loading a load the toy collapsed (the tests were carried out in accordance with the requirements of the harmonized standard ČSN EN 71-1).  The product doesn’t comply with the requirements of the Government Order No. 86/2011 Coll., on Technical Requirements for Toys.

Thus, during the use of the toy, a small child may be injured by the unsecured ends of the metal pipes, or the stroller may collapse due to its insufficient strength.

The Czech Trade Inspection Authority imposed a protective measure on the importer and distributor of the toy, which is to prohibit the distribution and withdraw the product from the market or from circulation. The toy was reported to the contact point at the Ministry of Industry and Trade and was published in RAPEX.

Detected defect of the toy – missing protective parts

Informace o výrobku:

Product name:				Kočárek golfky

Trademark:				„Doll Carrier“

Type / model number:			NO 0881M

EAN:					8592386005608

Identification data of manufacturer:	Xinyuanda toys factory, Chenghai district, Shantou city, Guangdong

Identification data of distributor:	LAMPS, a.s., Ve žlíbku 2906/1b, Praha 9, 193 00

Země původu:				China