|  | PRESS RELEASE |
| --- | --- |

One fuel sample failed in June

(Prague, 30 July 2020) The Czech Trade Inspection Authority carried out fuel quality inspections in June. It took 223 fuel samples at filling stations in the Czech Republic, and only 1 sample of E85 ethanol did not meet the quality requirements.

In June 2020, the Czech Trade Inspection Authority carried out checks on the quality of fuel in the Czech Republic.

CTIA officers took 223 fuel samples (automotive petrol, diesel, mixed fuel, biofuel, LPG, CNG and ethanol E85) and 1 sample did not meet the quality requirements, representing 0.4 % of non-compliant samples in the overall assessment.

Samples of DFB 30 and FAME fuel were not taken this month due to developments in the fuel market.

Automotive petrol

A total of 84 samples of automotive petrol were taken and inspected by the Czech Trade Inspection Authority in June 2020. In connection with the deep decline in sales of automotive petrol as a result of the coronavirus epidemic, the Czech Trade Inspection Authority allowed fuel dealers to sell stockpiles of automotive petrol at filling stations and to tolerate deviations of the parameter "vapour pressure" and to consider these samples as safe in the range of 60 - 90 kPa to 30 June, 2020.

Ethanol E85

In June 2020, 1 sample of ethanol E85 fuel was taken and inspected. The sample taken and controlled did not comply with the limit values of the tested indicator "vapour pressure" in ČSN EN 15293 - Motor fuels - Ethanol E85 - Technical requirements and methods of testing. The detected value was 27.7 kPa (minimum value is 34.1 kPa when measurement uncertainty is taken into account, maximum value is 60,9 kPa when measurement uncertainty is taken into account). And the detected value 0.834 % m/m was measured in the tested indicator "water", (maximum value is 0,416 % m/m when measurement uncertainty is taken into account).

Biofuels in fuels

In the monitored period the content of fatty acid methyl esters was inspected in 111 diesel fuel samples. The ethanol content in automotive petrol was inspected in 84 samples. Laboratory analysis showed that the upper limit of the content of bio-constituents wasn’t exceeded in any diesel fuel sample.

Taken action

In June 2020, the Czech Trade Inspection Authority imposed one measure prohibiting the sale of fuel that did not meet the quality and composition requirements set out in the implementing legislation, special legal regulations and Czech technical standards. The measure was issued for 1,382 l of fuel (ethanol E85) in the value amounting to CZK 38,557.80.

Results of the fuel quality control according to inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring and monitoring of fuels quality – June 2020 (2 pages)