|  | PRESS RELEASE |
| --- | --- |

A petrol sample failed in July

(Prague, September 1, 2020) The Czech Trade Inspection Authority continued to inspect the fuels quality in July. 1 of 284 taken samples did not comply with the quality requirements. It was an automotive petrol sample.

In July, the Czech Trade Inspection Authority carried out a quality inspection of fuel (automotive petrol, diesel, LPG, CNG). Filling stations in the Czech Republic were inspected. Out of a total of 284 samples taken, 1 did not comply with the quality requirements. It was a sample of automotive petrol.

Compared to June, the quality of automotive petrol samples worsened from 0.0% to 0.9% in July. Samples of Diesel Fuel Blend (DFB 30) and FAME were not taken in July 2020 due to the developments in the fuel market.

In July 2020, the Czech Trade Inspection Authority imposed in one case a ban on the sale of fuel that did not meet the quality and composition requirements as set out in the implementing legal regulation, special legal regulations and Czech technical standards. The measure was imposed on 10,380.35 litres of fuel (BA 98 Super plus) in the value amounting to CZK 331,133.17.

Automotive petrol

A total of 112 samples of automotive petrol were taken and inspected by the Czech Trade Inspection Authority in July 2020. 1 sample did not meet the quality requirements of the applicable technical standard. The inspected sample did not meet the following quality parameters: "Motor octane number", where the measured value of this quality parameter was 84.5 (minimum value including measurement uncertainty is 87.5); "Research octane number", when the measured value of this quality parameter was 94.7 (minimum value is 97.6 when measurement uncertainty is included), "end of distillation", where the measured value of this quality parameter was 310.5 °C (maximum value is 214.0°C when the measurement uncertainty is included). Other inspected and analysed samples of automotive petrol met the quality parameters set out in the technical standard ČSN EN 228+A1/Z1/O1 — Motor Fuels — Unleaded automotive petrol — Technical requirements and Test Methods.

There was a surplus of motor petrol in the quality satisfying the transition period due to the sharp decline in demand, caused by the impact of the COVID-19 pandemic measures. The market saw also the lack of production and distribution of motor petrol of summer quality caused by the two-month shutdown of the UNIPETROL Litvínov refinery and due to the emergence of a physic-chemical phenomenon of the so-called mixing effect (specified in CSN EN 228). Therefore, the Czech Trade Inspection Authority allowed fuel dealers to sell stockpiles of automotive petrol at petrol stations and to tolerate deviations of the parameter "vapour pressure" and to assess these samples safe in the range from 45 to 65 kPa from July 1, 2020, to July 15, 2020.

Organic ingredients in fuels

In the monitored period the content of fatty acid methyl esters was inspected in 139 diesel fuel samples. The ethanol content in automotive petrol was inspected in 112 samples. Laboratory analysis showed that the upper limit of the content of bio-constituents wasn’t exceeded in any diesel fuel sample.

Inspection results of fuels quality – individual inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring and monitoring of fuels quality – July 2020 (2 pages)

No. 2 - Monitoring and monitoring of fuels quality – January to July 2020 (2 pages)