|  | PRESS RELEASE |
| --- | --- |

A diesel sample failed in September

(Prague, October 30, 2020) The Czech Trade Inspection Authority regularly monitors the quality of fuel throughout the Czech Republic. In September, 229 samples were taken and inspected and 1 diesel sample did not comply with the quality requirements.

In September 2020, the Czech Trade Inspection Authority carried out an inspection on fuel quality (automotive petrol, diesel, biofuel, LPG, CNG and ethanol E85). This regular monitoring and monitoring of fuel quality is carried out in the form of sampling and laboratory analyses.

In September, CTIA officers took 229 fuel samples and 1 diesel sample did not meet the quality requirements.

Compared to August, there was an improvement in the sample of automotive petrol taken in September, as 1 sample of petrol failed in August. The deterioration occurred for diesel, as in August all diesel samples were compliant and 1 diesel sample failed in September.

Samples of blended fuel DFB 30 and FAME were not taken in September 2020 due to developments in the fuel market.

Diesel

In September 2020, the Czech Trade Inspection Authority took and inspected a total of 108 diesel samples. Of these number of samples taken and inspected, 1 sample did not meet the quality requirements of the applicable technical standard. The inspected diesel sample did not meet the quality parameter "flash point", where the measured value of this quality parameter was 42.0°C (minimum value is was 53.0°C when the measurement uncertainty is taken into account). The other diesel samples inspected and analysed met the quality requirements set out in technical standard „ČSN EN 590+A1 - Motor fuels - Diesel fuels - Technical requirements and Test Methods“ in connection with the requirements of Decree No. 133/2010 Coll., on Requirements for Fuel, on how to monitor the composition and quality of fuels and on their registration (Fuel Quality and Registration Decree).

Biofuels in fuels

In the monitored period the content of fatty acid methyl esters was inspected in 108 diesel fuel samples. The ethanol content in automotive petrol was inspected in 85 samples. Laboratory analysis showed that the upper limit of the content of bio-constituents wasn’t exceeded in any diesel fuel sample.

Imposed measures

The Czech Trade Inspection Authority prohibited a ban on the sale of 8,924 litres of fuels in the value amounting to CZK 281,106.00.

Results of inspection of the fuels quality according to individual inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring and monitoring of fuels quality – September 2020 (2 pages)

No. 2 - Monitoring and monitoring of fuels quality – January to September 2020 (2 pages)