|  | PRESS RELEASE |
| --- | --- |

In October, two taken diesel samples failed

(Prague, 2 December 2020) The Czech Trade Inspection Authority inspected the quality of fuel in October 2020. It took 175 fuel samples and two diesel samples did not meet the quality requirements.

In October this year, the Czech Trade Inspection Authority monitored the quality of fuel in the Czech Republic. It took 175 fuel samples at filling stations. 2 taken diesel samples did not comply with the quality requirements.

Fuel quality inspections and monitoring (automotive petrol, diesel, LPG, CNG and ethanol E85) were carried out in the form of sampling and laboratory analysis.

Compared to September, diesel samples worsened from 0.9% to 2.2% in October, as one diesel sample did not comply in September.

Samples of diesel fuel blend DFB 30 and FAME fuel were not taken in October 2020 due to the developments in the fuel market.

Diesel

In October 2020, the Czech Trade Inspection Authority took and inspected in total 90 diesel samples. 2 samples did not meet the quality requirements of the applicable technical standard. The inspected diesel samples failed the "flash point" quality parameter, when the measured value of this quality parameter was 48.5°C (minimum value 53.0°C when measurement uncertainty is included) and in the quality parameter "sulphur", where the measured value of this quality parameter was 25).2 mg/kg (maximum value is 11.8 mg/kg when the measurement uncertainty included). The other inspected diesel samples met the quality parameters set out in the technical standard ČSN EN 590+A1 - Motor fuels - Diesel fuels - Technical requirements and Test Methods in connection with the requirements of Decree No. 133/2010 Coll., on requirements for fuels, how to monitor and monitor the composition and quality of fuels and on their registration (Decree on Quality and Registration of Fuels).

Biofuels in fuels

In the monitored period, the content of fatty acid methyl esters was inspected in 90 diesel fuel samples. The ethanol content in automotive petrol was inspected in 62 samples. Laboratory analysis showed that the upper limit of the content of bio-constituents wasn’t exceeded in any diesel fuel sample.

Imposed measures

In October 2020, in two cases, the Czech Trade Inspection Authority imposed a ban on the sale of fuel that did not meet the quality and composition requirements set out in the implementing legislation, special legislation and Czech technical standards. The measures were imposed on 5,939.30 litres of fuel in the value of CZK 166,548.36.

Results of inspection of the fuels quality according to individual inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments: 	No. 1 - Monitoring and monitoring of fuels quality – October 2020 (2 pages)

No. 2 - Monitoring and monitoring of fuels quality – January to October 2020 (2 pages)