|  | PRESS RELEASE |
| --- | --- |

CTIA warns against the charger SWISSTEN CLT304 – high risk of injury from electric current

## (Prague, April 9, 2021) The Czech Trade Inspection Authority found a dangerous USB charger in the market of the Czech Republic, which can pose a high risk of electric shock to consumers. It is the product of the SWISSTEN CLT304 USB charger. The Czech Trade Inspection Authority imposed a ban on the supply of the product to the market and the immediate withdrawal of the product from the market.

The Czech Trade Inspection Authority detected the SWISSTEN CLT304 battery charger in a plastic bed and paper packaging. The following information is on the product: SWISSTEN; TRAVEL CHARGER; CLT304; CE marking; INPUT: AC 100-240V, 50Hz 60Hz; OUTPUT: DC 5V 2400 mA, mark of the protection class II. The following information is on the packaging: SWISSTEN; TRAVEL CHARGER; MICRO USB; 2.4A; product code 22013500; Producer: SWISSTEN Technology, Shenzhen, China; Importer: GAMACZ CZ s.r.o., Czech Republic, www.gamacz.cz; Input voltage: 100V to 240V; Output voltage: 5V; Output current 2400mA; Frequency: 50Hz - 60Hz; Temperature of use: 0-45 °C; EAN 8595217440630.

The CTIA identified a high risk of electric shock consumer injury or even death in the product by touching the USB connector on the product body, which reveals a dangerous 230V mains voltage due to the penetration of insufficient insulation between the primary and secondary parts of the product. Furthermore, it found non-compliant product markings – no information abou the trade name and contact address of the manufacturer, contact address of the importer and no nominal value of the input electric current.

The Czech Trade Inspection Authority imposed a ban on the seller from the supply of the product to the market and the immediate withdrawal of that product from the market. The product was reported to the contact point at the Ministry of Industry and Trade, product information was published in RAPEX.

Product information:

Product name:	  		USB nabíječka
Type / model No.:		SWISSTEN CLT304
Production no./EAN:		8595217440630
Identification of manufacturer:	SWISSTEN Technology, Shenzhen, China
Identification of importer:	GAMACZ.CZ s.r.o., Komenského 266, 54701 Náchod
Distributor:			F-communication s.r.o., Husovo náměstí 147, 34101 Horažďovice
Country of origin:		China