|  | PRESS RELEASE |
| --- | --- |

One diesel sample failed in March

(Prague, 27 April 2021) The Czech Trade Inspection Authority inspected the quality of fuel in March. In total, it took 273 fuel samples at domestic filling stations. One diesel sample did not meet the quality requirements. It also imposed a sales ban on 2,239.00 litres of fuel in the value amounting to CZK 66,946.10.

The Czech Trade Inspection Authority continued to inspect the quality of fuels in March 2021. In total, it took 273 fuel samples and 1 diesel sample did not meet the specified quality requirements.

An improvement from 1.9% to 0.4% in the number of non-compliant samples was seen in the overall assessment and comparison of the quality of fuel samples taken in March compared to February (4 fuel samples taken in February). As regards each fuel type, compared to February, a deterioration in diesel samples was seen from 0.0% in February to 0.8% in March. Improvements were seen in LPG samples taken from 14.3% to 0.0% and ethanol E85 from 100.0% to 0.0%.

Due to developments in the fuel market, samples of diesel fuel blend, B10 diesel, fame-high diesel, paraffin diesel, bio-CNG, LNG and bio-LNG were not taken in March.

In one case, the Czech Trade Inspection Authority prohibited the sale of fuel that did not meet the quality and composition requirements laid down by the implementing legislation, special legislation and Czech technical standards. The measure was imposed on 2,239.00 litres of fuel amounting to CZK 66,946.10.

Diesel

In March 2021, the Czech Trade Inspection Authority took and inspected a total of 131 diesel samples, including 1 sample that did not meet the quality requirements of the applicable technical standard. The diesel sample failed the quality parameter "oxidation stability", where the measured value of this quality parameter was 57 g/m3 (maximum value is 33 g/m3 when measurement uncertainty is taken into account. The other diesel samples inspected and analysed met the quality parameters set out in the technical standard ČSN EN 590+A1 – Motor fuels - Diesel fuels – Technical requirements and test methods in connection with the requirements of Decree 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Fuel Act.

Biofuels in fuels

During the monitored period, the content of fatty acid methyl esters was inspected in 107 samples of diesel. The ethanol content of automotive petrol was inspected in 84 samples. Laboratory analyses did not indicate that the permissible upper limit of the biofuel content was exceeded in samples of the monitored motor fuels.

Results of the inspection of fuels quality according to individual CTIA inspectorates:

Legenda: OD = odebráno, N = nevyhověl

Legend: COLL = collected, N = noncompliant

Attachments:

č. 1 - Monitoring of fuel quality – March 2021

č. 2 – Monitoring of fuel quality – January to March 2021