|  | PRESS RELEASE |
| --- | --- |

CTIA banned a light chain in the market - risk of electric shock

(Prague, 25 June 2021) The Czech Trade Inspection Authority (CTIA) found that there is dangerous electrical equipment in the domestic market. It is a light chain offered and sold under the name LED DIODS 3x20 Svítící koule.

The Czech Trade Inspection Authority detected the offer and sale of this dangerous product in the Czech Republic - a light chain LED DIODS 3x20 Svítící koule with non-replaceable light sources. The product is equipped with an electronic unit for the creation of light effects and an extendable double-pole fork. The following is displayed on the product: CE, brief safety information in Czech language (also in SK and PL) where it was stated among others "Light sources (bulbs) are not replaceable", 230V/50Hz, a mark for alternating current. On the electronic unit consumers can see: LED, 12V-250V 50Hz. LED DIODS 3x20 Svítící koule, 3x koule, 2.1m for indoor use only, brief instructions for use of the product and safety instructions in Czech language, which stated, among other things, "Light sources (bulbs) are not replaceable", 3x spheres, 230V, power supply 230V/50Hz, rated for 230V/50Hz, rated for 2.1m. Luminaire value 12V, luminaire protection class II/Ip20, CE, mark for appliance of Protection Class II, ITEM No.: 4241212, EAN 8713142412120 and Distribution.

There is a serious risk to the consumer when using the product because:

1. the power supply lead is not securely anchored to the electronic lighting effects unit and is not sufficiently secured against pulling out (connected only by fusing and soldering). If the lead is tampered with, the lead may be pulled out of the unit, exposing live parts of the product. The user touches a live part of the product that is energized, and serious injury or death to the user by electric shock will result.

2. the mechanical strength of the electronic lighting effects unit is not sufficient, the cover can be easily removed from the controller by hand without using any force or any tool, thereby making the parts of the product under power. The user touches this part of the product, and serious injury or death of the user by electric shock will occur.

The Czech Trade Inspection Authority imposed a protective measure on the seller, consisting of the immediate withdrawal of the product, which had already been placed on the market. The product was reported to the contact point at the Ministry of Industry and Trade and information about it was published in RAPEX.

Information on the product:

LED DIODS 3x20 Illuminating sphere

Product name:  	                                           		LED DIODS 3x20 Svítící koule
Model type:					světelný řetěz / model LED DIODS 3x20
EAN:						8713142412120
Identification of the manufacturer:		neuvedeny
Identification of the importer:			Comfort life s.r.o., Kubánské nám. 1391/11, Praha 10
Distributor:					Comfort life s.r.o., Kubánské nám. 1391/11, Praha 10
Country of origin:				China