|  | PRESS RELEASE |
| --- | --- |

One inspected fuel sample failed in May

(Prague, 28 June 2021) The Czech Trade Inspection Authority monitored the quality of fuels. In May, it took 255 samples of fuels throughout the Czech Republic and 1 sample taken and inspected failed the quality requirements.

In May, the Czech Trade Inspection Authority took 255 samples of fuels at domestic filling stations. 1 sample of ethanol E85 did not meet the quality requirements.

Samples of FAME, diesel fuel blend, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG and bio-LNG were not taken in May 2021 due to developments in the fuel market.

In the overall assessment and comparison of the quality of the fuel samples taken in May compared to April 2021, a deterioration from 0.0% to 0.4% in the number of non-compliant samples was observed, as all fuel samples inspected in April were compliant.

Automotive petrol

In connection with the measures taken as a result of the Covid-19 pandemic and in view of the stock levels of automotive petrol at manufacturers, distributors and filling stations, the Czech Trade Inspection Authority tolerates a vapour pressure value in the range of 45-70 kPa until 30 June 2021 and considers such petrol to be safe in terms of this parameter.

Ethanol E85

In the month of May 2021, 1 sample of ethanol E85 fuel was collected and inspected. The sampled and inspected sample did not comply with the limit values of EN 15293 - Motor fuels - Ethanol E85 - Technical requirements and test methods in the tested parameter 'Karl Fischer water', the value found was 0,835 % m/m (maximum value including measurement uncertainty 0,416 % m/m).

Biofuels in fuels

During the period under review, the fatty acid methyl ester content of 117 diesel samples was monitored. The ethanol content of automotive petrol was inspected in 109 samples. The laboratory analyses did not reveal any exceedance of the permissible upper limit for the content of bio-components in the samples of monitored motor fuels.

Measures imposed

In May, the Czech Trade Inspection Authority imposed one measure consisting of a ban on the sale of fuels that did not meet the quality and composition requirements set out in the implementing legislation, special legislation and Czech technical standards. The measure was imposed on 379.00 litres of fuel with the value amounting to CZK 9,437.10.

Results of the inspection of fuels quality according to individual CTIA inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments:

No. 1 - Monitoring of fuel quality – May 2021

No. 2 – Monitoring of fuel quality – January to May 2021