|  | PRESS RELEASE |
| --- | --- |

The CTIA banned two models of children's headbands

(Prague, 22 July 2021) The Czech Trade Inspection Authority (CTI) found that there are toys in the domestic market that may pose a risk to children. These are two models of plastic glowing headbands.

The Czech Trade Inspection Authority detected two dangerous toys in the Czech market. These are red plastic headbands with two horns. On the top, between the horns, there is a heart-shaped casing. The two parts of the case are connected by simply sliding the protrusions on one of the parts into the other part. The case contains in one case four button batteries, in the other case only two. When the fuse is removed and the switch is pressed, the headlamps light up or flash.

The toys are packaged in transparent bags with paper labels stuck on them stating "Not suitable for children under three" and CE marking in wrong graphics.

Both models are not in compliance with the requirements of the Government Decree No 86/2011 Coll., on the safety of toys, which are specified in EN 62115 - Electric toys - Safety. The requirement of Article 14.6 of the cited standard states that "Button cells and batteries of type R1 shall not be accessible without the use of a tool unless the cover of their compartment can only be opened after at least two simultaneous independent movements." This requirement applies to all toys.

The Czech Trade Inspection Authority has found that the cases in which the batteries of the toy models are stored can be opened without the use of a tool simply by opening the two plastic parts, which can be easily separated if the plastic protrusions are released from the holes on the other part. Once removed from the case, the batteries can be placed in the child's mouth and swallowed or inhaled.

Toy model 1 (Toy model 2 has two cell batteries)

Open housing with cell batteries

The Czech Trade Inspection Authority imposed a protective measure on the seller pursuant to Section 18a(4) of Act No. 22/1997 Coll., which is the immediate withdrawal of the products from distribution. The toy models were reported to the contact point at the Ministry of Industry and Trade and published in the RAPEX system.

Information about the products

Toy model 1

Product name on the product:		Čelenka – rohy na svitri

Model type/ number:			ITEM NO: HLT7193

EAN:					6926450471938

Toy model 2

Product name on the product:		Rohy na svitri

Model type/ number:			ITEM NO: HLT7195

EAN:					6962019042959

Applicable for both toys:

Identification of importer:		HOME COMFORT s.r.o., Libušská 319, Praha 4

Identification of manufacturer:	Not displayed

Distributor:	Dinh Thieu Nguyen, náměstí Karla IV. 6, 362 21, Nejdek

Country of origin:	Made in China

Photos of products, horns are offered with rough and smooth surface