|  | PRESS RELEASE |
| --- | --- |

CTIA bans dangerous reindeer-shaped light chain

(Prague, 10 August 2021) The Czech Trade Inspection Authority has detected a dangerous reindeer-shaped Christmas light chain in the domestic market. If the user touches a live part of the product that is under voltage, they can be seriously injured or even killed by the electric current.

The Czech Trade Inspection Authority has found that a Christmas light chain sold under the name Reindeer LED Light Chain is offered to consumers in the market of the Czech Republic. This electrical product does not have replaceable light sources, is equipped with an electronic unit for the creation of lighting effects and a retractable two-pole fork. The product and the product packaging are marked with the following: CE marking of conformity, 220-240 v, 50Hz, model V8F50, mark of conformity, mark of class V8F50. protection mark II, indoor use mark, AC mark, IP20, brief instructions for use were enclosed with the product and were provided in the Czech language. Manufacturer Huashun Lightng Co., Ltd., importer OHNIVÁK EURO SRO.

The Czech Trade Inspection Authority found the cause of the hazard in the power supply lead. It is not securely anchored to the electronic unit for lighting effects and not sufficiently secured against pulling out (connected only by fusible material and soldering). If the user manipulates with the lead, the lead can be pulled out of the unit. This will result in live parts of the product being exposed. The user touches a live part of the product that is under voltage, and serious injury or death to the user by electric shock can be the result.

Action taken:

The CTIA has imposed a protective measure on the seller pursuant to Section 50(3) of Act No. 90/2016 Coll., on conformity assessment of selected products when made available in the market. The measure consisted in the immediate withdrawal of the product, which is dangerous and had already been placed on the market. The product has been reported to the contact point at the Ministry of Industry and Trade and information about it has been published in the RAPEX system.

Product information

Název výrobku:  	                                           Světelný řetěz LED diody Sob

Model type / number:				light chain / model V8F50

EAN:						201955667885

Identification data of manufacturer:                      Huashun Lightng Co., Čína

Identification data of importer:			OHNIVÁK EURO SRO.

Distributor:	              Loat Nguyen Van, Poštovní 924, 35731 Horní Slavkov,

Country of origin:	China