|  | PRESS RELEASE |
| --- | --- |

Two fuel samples tested in January failed

(Prague, March 8, 2022) The Czech Trade Inspection Authority inspected the quality of fuels in January. A total of 198 samples were taken and two diesel samples failed to meet the required quality parameters.

The Czech Trade Inspection Authority inspected the quality of fuels at filling stations across the Czech Republic in January. It took and inspected 198 fuel samples, including 2 samples that failed to meet the quality requirements.

Compared to December 2021, there was a deterioration as one fuel sample (LPG) failed in December.

Samples of FAME, diesel fuel blend, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG, bio-LNG and ethanol E85 were not sampled in January due to fuel market developments.

Diesel

In January 2022, the Czech Trade Inspection Authority collected and inspected a total of 95 diesel fuel samples. Of these samples taken and inspected, 2 samples did not meet the quality requirements of the applicable technical standard. The inspected diesel fuel samples failed to comply with the quality parameter 'flash point', where the measured value of this quality parameter was 34,5 °C in one case, and 41,0 °C in the other case (the minimum value including the measurement uncertainty is 53,0 °C). In the case of the second non-compliant finding, this was a verification analysis after a new fuel load at the same filling station. A second verification analysis of the same fuel after a re-fueling was already without any defect. The other samples of diesel inspected and analysed met the quality parameters laid down in the technical standard ČSN EN 590+A1 - Automotive fuels - Diesel - Technical requirements and test methods in connection with the requirements of Decree 516/2020 Coll., on fuel requirements and implementation of certain other provisions of the Act on Fuels.

Bio fuels in motor fuels

During the monitored period, the content of fatty acid methyl esters was inspected in 95 samples of diesel. The ethanol content of automotive petrol was inspected in 76 samples. Laboratory analyses did not indicate that the permissible upper limit of the biofuel content was exceeded in samples of the monitored motor fuels.

Results of fuel quality inspections by individual inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments:

č. 1 - Monitoring of fuel quality – January 2022