|  | PRESS RELEASE |
| --- | --- |

One diesel sample failed in April

(Prague, 26 May 2022) The Czech Trade Inspection Authority monitored the quality of fuel in April. It took 189 fuel samples at domestic filling stations all across the Czech Republic, finding out that 1 diesel sample failed the quality requirements.

The Czech Trade Inspection Authority monitored the quality of fuels in the Czech Republic in April. It took a total of 189 fuel samples at filling stations. One diesel fuel sample did not meet the quality requirements.

Compared to March, a deterioration was seen in April, as all fuel samples inspected in March complied with the requirements.

Samples of FAME, diesel fuel blend, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG, bio-LNG and E85 ethanol were not taken in April due to the fuel market developments.

| Taken fuel samples according to types - April 2022 |
| --- |
| Fuel type | Taken samples | Ratio | Noncompliant samples | Ration of fuel type |
| Petrol | 74 | 39.15 | 0 | 0.0 |
| Diesel | 88 | 46.56 | 1 | 1.1 |
| FAME | 0 | 0.0 | 0 | 0.0 |
| Diesel fuel blend | 0 | 0.0 | 0 | 0.0 |
| B10 diesel | 0 | 0.0 | 0 | 0.0 |
| High FAME diesel | 0 | 0.0 | 0 | 0.0 |
| Paraffini diesel | 0 | 0.0 | 0 | 0.0 |
| LPG | 24 | 12.70 | 0 | 0.0 |
| CNG, bio-CNG | 3 | 1.59 | 0 | 0.0 |
| LNG, bio-LNG | 0 | 0.0 | 0 | 0.0 |
| Ethanol E85 | 0 | 0.0 | 0 | 0.0 |
| Total | 189 | 100.0 | 1 | 0.5 |

Diesel

In the month of April, the Czech Trade Inspection Authority took and inspected a total of 88 diesel fuel samples. Out of this number of samples taken and inspected, 1 sample did not meet the quality requirements of the applicable technical standard. The sample of diesel inspected failed the quality parameter 'flash point', where the measured value of this quality parameter was 43.0 °C (minimum value, including the measurement uncertainty, is 53.0 °C). The other samples of diesel fuel inspected and analysed met the quality parameters set out in the technical standard ČSN EN 590+A1 - Motor fuels - Diesel fuels - Technical requirements and test methods, in relation to the requirements of Decree No. 516/2020 Coll., on fuel requirements and implementation of certain other provisions of the Act on Fuels.

Bio fuels in motor fuels

During the monitored period, the content of fatty acid methyl esters was inspected in 88 samples of diesel. The ethanol content of automotive petrol was inspected in 74 samples. Laboratory analyses did not indicate that the permissible upper limit of the biofuel content was exceeded in samples of the monitored motor fuels.

Attachments:

č. 1 - Monitoring of fuel quality – April 2022

č. 2 – Monitoring of fuel quality – January to April 2022