|  | PRESS RELEASE |
| --- | --- |

One diesel and one petrol sample failed in June

(Prague, 10 August 2022) The Czech Trade Inspection Authority inspected the fuels quality in June 2022. A total of 212 samples were taken and 2 samples of fuels failed to meet the quality requirements.

The Czech Trade Inspection Authority continued its fuel quality inspections in June 2022. In this month, it took a total of 212 fuel samples at petrol stations across the Czech Republic. Two samples failed to meet the specified quality requirements - 1 sample of petrol and 1 sample of diesel.

Compared to May, a deterioration was recorded in June, as 1 sample of LPG taken in May did not comply.

Samples of FAME, diesel fuel blend, B10 diesel, high FAME diesel, paraffinic diesel, bio-CNG, LNG, bio-LNG and E85 ethanol were not sampled in June due to fuel market developments.

| Taken fuel samples according to types - July 2022 |
| --- |
| Fuel type | Fuel type | Fuel type | Fuel type | Fuel type |
| Petrol | 83 | 39,2 | 1 | 1,2 |
| Diesel | 103 | 48,6 | 1 | 1,0 |
| FAME | 0 | 0,0 | 0 | 0,0 |
| Diesel fuel blend | 0 | 0,0 | 0 | 0,0 |
| B10 diesel | 0 | 0,0 | 0 | 0,0 |
| High FAME diesel | 0 | 0,0 | 0 | 0,0 |
| Paraffini diesel | 0 | 0,0 | 0 | 0,0 |
| LPG | 24 | 11,3 | 0 | 0,0 |
| CNG, bio-CNG | 2 | 0,9 | 0 | 0,0 |
| LNG, bio-LNG | 0 | 0,0 | 0 | 0,0 |
| Ethanol E85 | 0 | 0,0 | 0 | 0,0 |
| Total | 212 | 100,0 | 2 | 0,9 |

Automotive petrol

In June 2022, the Czech Trade Inspection Authority collected and inspected a total of 83 samples of automotive petrol. Out of this number, 1 sample did not meet the quality requirements of the applicable technical standard. The inspected sample failed the quality parameter 'vapour pressure', where the measured value of this quality parameter was 74.9 kPa (while the maximum value including the measurement uncertainty is 60.9 kPa). The other samples of automotive petrol inspected and analysed met the quality parameters set out in the technical standard EN 228+A1/Z1/O2 - Motor fuels - Unleaded automotive petrol - Technical requirements and test methods.

In connection with the market volatility due to the current crisis, the Czech Trade Inspection Authority has taken into account the state of existing stocks of automotive petrol at manufacturers, distributors and filling stations and tolerates the value of the parameter 'vapour pressure' in the range of 45 to 70 kPa in the period from 22 May 2022 to 30 June 2022 and considers such automotive petrol to be safe in terms of this parameter.

Diesel

In June 2022, the Czech Trade Inspection Authority took and inspected a total of 103 diesel fuel samples. 1 sample did not meet the quality requirements of the applicable technical standard. The inspected diesel fuel sample failed in the quality parameter 'oxidation stability', where the measured value of this quality parameter was 649 g/m3 (the maximum value including the measurement uncertainty is 33 g/m3). The other samples of diesel fuel inspected and analysed met the quality parameters set out in the technical standard ČSN EN 590+A1 - Motor fuels - Diesel fuels - Technical requirements and test methods in relation to the requirements of Decree 516/2020 Coll., on requirements for fuels and implementation of certain other provisions of the Fuel Act.

Organic fuels in fuels

During the monitored period, the content of fatty acid methyl esters was inspected in 103 samples of diesel. The ethanol content of automotive petrol was inspected in 83 samples. Laboratory analyses did not indicate that the permissible upper limit of the biofuel content was exceeded in samples of the monitored motor fuels.

Imposed measures

In June 2022, the Czech Trade Inspection Authority imposed in one case a ban on the sale of fuels that did not meet the quality and composition requirements set out in the implementing legislation, special legislation and Czech technical standards. The measure was issued for 14,006.91 litres of fuel with a value of CZK 642,917.17.

Results of fuel quality inspections by individual inspectorates:

Legend: COLL = collected, N = noncompliant

Attachments:

č. 1 - Monitoring of fuel quality – June 2022

č. 2 – Monitoring of fuel quality – January to June 2022