|  | PRESS RELEASE |
| --- | --- |

CTIA banned a dangerous LED doorbell in the market

(Prague, 28 June 2023) The Czech Trade Inspection Authority (CTIA) has found that there is an electrical device on the domestic market that may pose a risk to consumers. The product is sold as Merry Christmas - zvonek (doorbell).

The Czech Trade Inspection Authority (CTIA) has found that there is an electrical device in the Czech market which may pose a risk to consumers. The product is a bell Merry Christmas - light chain (Christmas lighting) intended for indoor use only with non-replaceable LED light sources equipped with an electronic unit for lighting effects, put in plastic packaging. On the product it is marked: CE, 220-240V, 50Hz, 2,5A, mark for protection class II, mark for alternating current, IP20, mark for indoor use, manufacturer Huashun Lighting Co. Ltd., importer Distributor.šperky obchod EU s.r.o. On the packaging is: marking of the manufacturer, importer, made in PRC, CE, 220-240V, 110V, EAN 8222205601208, V8F50, brief instructions for the use of the product.

The Czech Trade Inspection Authority has identified a serious risk with the product where the power supply lead is not securely anchored to the electronic unit and sufficiently secured against pulling out (connected only by fusible material and soldering). Handling of the lead may result in the lead being pulled out of the unit, thereby exposing live parts of the product. Furthermore, the mechanical strength of the electronic unit was found to be insufficient. The cover can be easily removed from the control unit by hand without force or tools, thereby exposing live parts of the product. In both cases, the user touches a live part of the product that is live and serious injury or death to the user by electric shock occurs.

The Czech Trade Inspection Authority imposed a ban on the seller (Article 50(3) of Act No. 90/2016 Coll., on the assessment of conformity of selected products when made available in the market) from supplying the product to the market, including products that have already been placed on the market. The product was reported to the contact point at the MIT and information about it was published in the Safety Gate system.

Product information:

Product name:  	                                           		Merry Christmas - zvonek

Model type / number:				LED Světelný řetěz/ V8F50

EAN:						8222205601208

Identification data of the manufacturer:               Huashun Lighting Co. Ltd.

Identification data of the importer:	              Distributor.šperky obchod EU s.r.o.

Distributor:	               MinhLHW s.r.o., Selbská 1204/9, 35201 Aš

Country of origin:	 China