|  | PRESS RELEASE |
| --- | --- |

CTIA banned a dangerous LED light chain in the market

(Prague, 27 June 2023) The Czech Trade Inspection Authority (CTIA) has found that there is electrical device in the domestic market that may pose a risk to consumers. The product is offered as LED Cristal Light.

The Czech Trade Inspection Authority (CTIA) has found that there is an electrical device in the Czech market that may pose a risk to consumers. The product is a light chain (Christmas lighting) intended for indoor use only with non-replaceable LED light sources equipped with an electronic unit for lighting effects in a paper cardboard packaging. On the product it is marked: CE, mark for TO II, 220-240V, mark for AC, 50Hz, Protection Class II/IP20, EAN 6954871268639, LG3224, model V8F50. On the packaging it says: LED Cristal LIGHT, BAJO CONSUMO DE ENERGIA, Conectar a CA, Model V8F50, 220-240V, mark for AC, 50Hz, Protection Trida II/IP20, EAN 1050864000004, user manual, safety instructions.

The Czech Trade Inspection Authority has identified a serious risk in the product where the power supply lead is not securely anchored to the electronic unit and sufficiently secured against pulling out (connected only by fusible material and soldering). Manipulation of the lead may result in the lead being pulled out of the unit, thereby exposing live parts of the product. Furthermore, the mechanical strength of the electronic unit was found to be insufficient. The cover can be easily removed from the control unit by hand without force or tools, thereby exposing live parts of the product. In both cases, the user touches a live part of the product that is live and serious injury or death to the user by electric shock occurs.

The Czech Trade Inspection Authority imposed a ban on the seller (Article 50(3) of Act No. 90/2016 Coll., on the assessment of conformity of specified products when they are supplied to the market) from supplying the product to the market, including products that have already been placed on the market. The product was reported to the contact point at the MIT and information about it was published in the Safety Gate system.

Product information:

Product name:  	                                 		LED Cristal Light

Model type/ number:				LED Světelný řetěz/V8F50

EAN:						6954871268639

Identification of manufacturer:v                               neuvedeny

Identification of importer:		              neuvedeny

Distributor:	               Van Quyen Nguyen, Palackého 1212/10, 35002 Cheb

Country of origin:	 China