|  | PRESS RELEASE |
| --- | --- |

Christmas chain for indoor use can be dangerous to consumers

(Prague, 14 July 2023) The Czech Trade Inspection Authority has found that a Christmas chain sold in the domestic market as 300L LED DECORATIVE LIGHTS is dangerous.

The Czech Trade Inspection Authority has found that an electrical device is offered in the market in the Czech Republic that may pose a risk to consumers. It is a light chain (Christmas lighting) intended for indoor use only with non-replaceable LED light sources equipped with an electronic unit for lighting effects in a paper cardboard packaging. The product is marked with CE mark for TO II, 25	0V, 2,5A, mark for AC, 50Hz, mark for protection class II, made in China, lindading s.r.o., pictogram not suitable for children 0 to 3 years. 300L LED DECORATIVE LIGHTS, brief instructions for use and safety instructions, CE, pictogram not suitable for children from 0 to 3 years, 23M+1.5M, made in China, lindading s.r.o., EAN 1040171360007, model H22-726-735.

This light chain presents a serious safety risk as the power supply lead is not securely anchored to the electronic unit and is not sufficiently secured against pulling out (only fused and soldered). If the lead is tampered with, the lead may be pulled out of the unit, thereby exposing live parts of the product. Furthermore, the mechanical strength of the electronic unit was found to be insufficient. The cover can be easily removed from the control unit by hand without using any force or a tool, thereby exposing live parts of the product. If the user touches live parts of the product, serious injury or death to the user by electric shock would result.

The Czech Trade Inspection Authority imposed a ban on the seller (Section 50(3) of Act No. 90/2016 Coll., on the assessment of conformity of selected products when made available in the market) from supplying the product to the market, including products already placed on the market. The product was reported to the contact point at the MIT and information about it was published in the Safety Gate system.

Product name:	  	                             300L LED DECORATIVE LIGHTS

Model type / number:			LED Světelný řetěz/H22-726-735

EAN:					1040171360007

Identification data of the manufacturer: not displayed

Identification data of the importer:	not displayed

Distributor:	 ABC - Shopping paradise s.r.o., Revoluční 1082/8,                                        11000 Praha 1

Country of origin:                                        China