|  | PRESS RELEASE |
| --- | --- |

LED hazardous light chain

(Prague, 20 July 2023) The Czech Trade Inspection Authority (CTI) has detected a dangerous electrical device in the domestic market, sold as Light Chain Karácsonyi jégcsap égösor.

The Czech Trade Inspection Authority has found that an electrical device is In the market of the Czech Republic that may pose a risk to consumers. It is a Christmas light chain with non-replaceable LED light sources equipped with an electronic unit in a plastic box. The product is marked CE, made in China, 2.5A, 50Hz, 250V, mark for AC. The packaging is marked CE, 13.5W, 50Hz, 200-240V, model DN75, brief instructions for use and safety instructions in foreign languages only.

The product has a serious safety risk for the consumer as the power supply lead is not securely anchored to the electronic unit and sufficiently secured against pulling out (connected only by fusion and soldering). If the lead is tampered with, the lead may be pulled out of the unit, exposing live parts of the product. In addition, the mechanical strength of the electronic unit is not sufficient as the cover can be easily removed from the driver by hand without force or tools, thereby exposing live parts of the product. If the user touches live parts of the product that are live, serious injury or death to the user by electric shock will result.

The Czech Trade Inspection Authority imposed a protective measure on the seller (Section 50(3) of Act No. 90/2016 Coll., on conformity assessment of selecter products when made available in the market), which is a ban on supplying the product to the market, including products already on the market. The product has been reported to the contact point at the MIT and information about it has been published in the Safety Gate system.

Product information:

Product name:  	                                      		Světelný řetěz Karácsonyi jégcsap égösor

Model no./type:				LED Světelný řetěz/DN75

EAN:						8595563688885

Identification data of the manufacturer:               not displayed

Identification data of the importer:	              not displayed

Distributor:	               Thi Kim Dung Bui, Okružní 1191, 36222 Nejdek

Country of origin:	 China