|  | PRESS RELEASE |
| --- | --- |

Dangerous Merry Christmas light chain

(Prague, 29 September 2023) The Czech Trade Inspection Authority has found that electrical equipment in the Czech market is being offered to consumers that may pose a risk to consumers. It is a Merry Christmas light chain, type/model number LED Light Chain/V8F50.

The Czech Trade Inspection Authority has found that a dangerous Christmas tree-shaped light chain with non-replaceable LED light sources equipped with an electronic unit in a plastic bag is being offered on the domestic market. CE mark for protection class II, 2.5A, 50Hz, 220-240V, AC mark for indoor use, IP20, made in PRC. CE, mark for protection class II, 2.5A, 50Hz, 220-240V, mark for alternating current, mark for indoor use, IP20, made in PRC, brief instructions for use are indicated on the packaging.

The product poses a serious safety risk to the consumer as the power lead is not securely anchored to the electronic unit and sufficiently secured against pulling out (connected by fusible link and solder only). If the lead is tampered with, the lead may be pulled out of the unit, exposing live parts of the product. In addition, the mechanical strength of the electronic unit is not sufficient as the cover can be easily removed from the driver by hand without the use of any force or a tool, thereby exposing live parts of the product. If the user touches live parts of the product that are live, serious injury or death to the user by electric shock could occur.

The CTIA has imposed a protective measure on the seller (pursuant to Section 50(3) of Act No. 90/2016 Coll., on Conformity Assessment of Selected Products when Made Available in the Market), which is a ban on supplying the product to the market or a ban on the sale of a product already on the market. The product has been reported to the contact point at the MIT and information about it has been published in the Safety Gate system.

Product information:

Product name:  	                                        Světelný řetěz Merry Christmas

Model type / number:				LED Světelný řetěz/V8F50

EAN:						8222205601260

Identification of manufacturer:                        Huashun Lightng  Co. Ltd., Qiantu, Dongcheng

Identification of importer:		             not displayed

Distributor:	              Van Thoan Do, Krušnohorská 1102, 36301 Ostrov

Country of origin:			             China