|  | PRESS RELEASE |
| --- | --- |

Dangerous LED light chain

(Prague, 2 October 2023) The Czech Trade Inspection Authority has found that a product offered in the domestic market is dangerous to consumers. It is a Christmas light chain sold as LED Light Chain/SD802-821.

The Czech Trade Inspection Authority has found that there is a dangerous Christmas lighting in the market - a light chain that is intended for indoor use only. It has non-replaceable LED light sources equipped with an electronic unit for lighting effects in a paper cardboard packaging. The product is marked CE, mark for TO II, 250V, 2.5A, mark for AC, 50Hz, mark for protection class II, IP44. The packaging is marked: brief instructions for use and safety instructions, CE, 220-240V, bulb voltage 9V, 0,068A, lindading s.r.o., EAN 2060113904006, model SD802-821.

The product poses a serious safety risk to the consumer as the power cord is not securely anchored to the electronic unit and is not sufficiently secured against pulling out (connected only by fusible material and soldering). If the lead is tampered with, the lead may be pulled out of the unit, exposing live parts of the product. In addition, the mechanical strength of the electronic unit is not sufficient as the cover can be easily removed from the driver by hand without using any force or tool, thereby exposing live parts of the product. If the user touches live parts of the product that are live, serious injury or death to the user by electric shock could result.

The Czech Trade Inspection Authority has imposed a protective measure on the seller (pursuant to Section 50(3) of Act No. 90/2016 Coll., on the assessment of conformity of specified products when they are supplied to the market), which is a ban on the supply to the market of the said product, which is dangerous and has already been placed on the market. The product has been reported to the contact point at the MIT and information about it has been published in the Safety Gate system.

Product information

Product name:  	                                        200L LED DECORATIVE LIGHTS

Model type / number:				LED Světelný řetěz/SD802-821

EAN:						2060113904006

Identification of manufacturer:                       not displayed

Identification of importer:		            not displayed

Distributor:	Van Luong Tran, Sokolovská 232/2, Kynšperk nad Ohří

Country of origin:					China